## Slide 1: WF on SLS baseline for NR MA
Huawei, HiSilicon, [CATT], [ZTE], [Samsung], [Nokia], [Intel],
3GPP TSG RAN WG1 #86 R1-168540
Gothenburg, Sweden, Aug. 22-26, 2016
Agenda item: 8.1.2.2

## Slide 2: Proposals
Baseline for providing absolute system level evaluation results for UL mMTC, for calibration purpose only
  CP-OFDM as the UL waveform
    UL DMRS overhead, 1 OFDM symbol out of 7 OFDM symbols
  A UE selects a MA physical resource randomly from a pool of orthogonal MA physical resources
    There is no partial overlapping between the MA physical resources selected by more than one UE
    All orthogonal MA physical resources are of same size
  Rx MMSE receiver, assuming ideal channel estimation
    No blind decoding assumed
  Same MCS for all UEs,
    MCS is reported by each company
  Open loop power control
    Alpha=1, P0= -90 dBm
  Packet size is fixed by [20] bytes
Note: The above assumptions only apply to the baseline, i.e. other assumptions can be used for evaluation of proposed non-orthogonal multiple access scheme(s)