## Slide 1: NR MIMO Initial Access Procedures
National Instruments
3GPP TSG RAN WG1 Meeting #86bis R1-1609722
Lisbon, Portugal 10th – 14th October 2016
Agenda item: 8.1.5
Source: National Instruments
Title: NR MIMO Initial Access Procedures
Document for: Discussion and Decision

## Slide 2: Forward Compatibility Problems with Current Access Procedure
Current LTE Protocol requires up to four of 14 symbols or time-frequencies resources per subframe to be allocated to Physical Downlink Control Channel (PDCCH).
Massive MIMO has already been demonstrated in experimental systems to support up to 20 channels of MU-MIMO. [1].
Channel Reciprocity based MIMO for above and below 6 GHz was discussed in RAN1#86 in following Way Forwards [2], [3], [4].
It is expected in the future for the amount of control resources required to support Massive MIMO to overwhelm any common control mechanism.
In order to ensure that in the NR spec, Massive MU-MIMO is fully enabled, a Multi-User PDCCH (MU-PDCCH) is needed.
Additionally, a random access procedure is required which is channel reciprocity-based in order to support reciprocity beamforming.

## Slide 3: Onboarding Users
In a Massive MU-MIMO system, one of the challenges in onboarding all of the users
One requirement of the initial access procedure is that it be capable of efficiently accomplishing this task
The use of reciprocity-based initial access is central to the onboarding of massive numbers of simultaneous users, as explained in this contribution.

## Slide 4: New Channels and Capabilities for Massive MU-MIMO
In order to support the full capabilities of Massive MU-MIMO, the following additional channels, signals and/or capabilities are required.
  Reciprocity-based Random Access
  Light PDCCH and Light PDSCH
    For system information and random access responses
    Can be potentially combined into one channel
  Reciprocity Reference Signals
  MU-PDCCH

## Slide 5: Scaling of MU-MIMO
PSS
SSS
Light-PDCCH and Light PDSCH
MU-PDCCH
Random Access Signals
Reciprocity Reference Signals
MU-PDSCH
MU-PUSCH
MU-PUCCH
MIMO Layers Required

## Slide 6: PDCCH and PDSCH
Some basic messaging such as System Information (SI) and Random Access Responses (RAR) are required. Today, they are sent on PDCCH and PUSCH, could potentially be combined onto one channel. Regardless, in order to support Massive MU-MIMO, common control should be minimized.
Proposal 1: Support light PDCCH and light PDSCH in New Radio for Massive MU-MIMO.

## Slide 7: Random Access Signals
Random Access Signals
  Up to eight antenna ports to be supported per UE.
  Root Chu, CS Chu and FD-Interleaving all considered for MUXing
  #Antennas at UE blind detected at eNB
  Wideband RACH considered for reciprocity
Proposal 2: Support enhancements to Random Access Signals as specified above

## Slide 8: Reciprocity Reference Signals, MU-PUSCH and MU-PDCCH
Reciprocity reference signals to be transmitted by UE
Sets up MU-PUSCH transmission with all of the associated start-up signaling
This enables reciprocity-based MU-PDCCH
Proposal 3: Support Reciprocity Reference Signals to enable MU-PDCCH and MU-PUSCH in New Radio for Massive MIMO.

## Slide 9: Proposals
Proposal 1: Support light PDCCH and light PDSCH in New Radio for Massive MU-MIMO.
Proposal 2: Support enhancements to Random Access Signals as specified above
Proposal 3: Support Reciprocity Reference Signals to enable MU-PDCCH and MU-PUSCH in New Radio for Massive MIMO.

## Slide 10: References
[1] P. Harris et.al, “Serving 22 Users in Real-Time with a 128-Antenna Massive MIMO Testbed”, To be presented at IEEE International Workshop on Signal Processing Systems (SIPS 2016), Dallas.
[2] R1-168254, WF on UL MIMO transmission, Huawei, HiSilicon, China Unicom, Samsung, NTT DOCOMO, RAN1#86.
[3] R1-168179 WF on CSI measurement and reporting in NR, Huawei, HiSilicon, Ericsson, China Telecom, RAN1#86.
[4] R1-168388 WF on beam management, CATT, Samsung, National Instruments, ZTE, RAN1#86.