## Slide 1: WF on Beam management
CATT, CATR, CMCC, Xinwei, Samsung
3GPP TSG RAN WG1 Meeting #86bis R1-1611014
Lisbon, Portugal, October 10th - 14th 2016
AI: 8.1.4.1

## Slide 2: Excerpts of agreements from RAN1#86
Agreements:
The following DL L1/L2 beam management procedures are supported within one or multiple TRPs:
  P-1: is used to enable UE measurement on different TRP Tx beams to support selection of TRP Tx beams/UE Rx beam(s)
    For beamforming at TRP, it typically includes a intra/inter-TRP Tx beam sweep from a set of different beams
    For beamforming at UE, it typically includes a UE Rx beam sweep from a set of different beams
    FFS: TRP Tx beam and UE Rx beam can be determined jointly or sequentially
Agreements:
RAN1 study different methods of determining Tx and Rx beam(s) for communication on one link direction (uplink or downlink), e.g.,
  Joint determination: Tx beam and Rx beam are determined jointly
  Separate determination: Tx beam or Rx beam are determined sequentially.
  Multi-stage determination: for instance, coarse Tx-Rx beam determination followed by fine Tx-Rx beam determination
Study beam management procedure with and without explicit signaling of beam(s) or beam group(s) used for transmission

## Slide 3: Proposals
NR supports multi-stage beam determination
  First-stage
    RSs for first stage are transmitted cell-specifically and periodically
  Following stage(s)
    RSs for other than first stage are transmitted UE(Group)-specifically
    Beamforming weights for the RSs are derived based on results of previous stage(s)
  FFS QCL relations between RSs of different stages
NR also supports beam determination without first stage
Both joint and sequential beam determination are supported in NR