## Slide 1: WF on Sync signal periodicity
Qualcomm, NTT DoCoMo, [Nokia, ASB, Intel, Samsung, Ericsson, Huawei, ] …
3GPP TSG RAN WG1 Meeting #87 R1-1613155
Reno, USA, 14th – 18th of November 2016
Agenda item: 7.1.2.1

## Slide 2: Background
Following agreement occurred in the previous RAN1 meeting [1]
NR defines at least two types of synchronization signals
  NR-PSS at least for initial symbol boundary synchronization to the NR cell
    FFS other functionality provided by NR-PSS, e.g., part of NR cell ID, serving as DMRS for NR-SSS, detection of subcarrier spacing
  NR-SSS for detection of NR cell ID or at least part or full of NR cell ID
    Number of NR cell IDs is targeted to be at least 504
      FFS: larger than that in LTE
      FFS number of NR cell IDs
    NR-SSS detection is based on the fixed time/freq. relationship with NR-PSS resource position irrespective of duplex mode and beam operation type at least within a given frequency range and CP overhead
      FFS FDM or TDM
    FFS other functionality provided by NR-SSS, e.g., demodulation of broadcast channel, RRM measurement, deriving subframe index, deriving symbol index
NR defines at least one broadcast channel: NR-PBCH
  NR-PBCH decoding is based on the fixed relationship with NR-PSS and/or NR-SSS resource position irrespective of duplex mode and beam operation type at least within a given frequency range and CP overhead
    FFS: Unlicensed spectrum case
  FFS relationship between NR-PBCH subcarrier spacing and NR-PSS and/or SSS subcarrier spacing
  Following broadcasting schemes to carry essential system information can be considered
    Option 1: NR-PBCH carries a part of essential system information for initial access including information necessary for UE to receive channel carrying remaining essential system information
    Option 2: NR-PBCH carries minimum information necessary for UE to perform initial UL transmission (not limited to NR-PRACH) in addition to information in Option 1
    Option 3: NR-PBCH carries all essential system information for initial access
    Other options are not precluded
1. R1-1610438, “WF on NR Initial Access Signals/Channels”, 3GPP TSG RAN WG1 Meeting #86 bis, Lisbon, Portugal

## Slide 3: WF on sync signal periodicity
SS burst set transmission is periodic
  At least for initial cell selection, UE may assume a default periodicity of SS burst set transmission for a given carrier frequency
    Exact value of default periodicity of SS burst set transmission for a given carrier frequency needs to be studied
  FFS:UE may be provided with updated information regarding the SS burst set periodicity by the network
    FFS: Validity duration of information
    Note: This does not imply SS-burst set needs to be always on with the updated periodicity
  Companies are encouraged to investigate the tradeoff between network flexibility/power consumption and UE complexity/power consumption.