## Slide 1: WF on Group-based Beam Management
3GPP TSG RAN WG1 Meeting #87 R1-1613740
Reno, USA, 14th – 18th November 2016
Agenda Item: 7.1.3.3
ZTE, ZTE Microelectronics, ASTRI

## Slide 2: Proposal-1
  Beam grouping according to the following properties should be supported
    Channel/beam properties observed by UE, e.g., angle of arrival for DL, delay, etc;
    Beam properties observed by TRP, e.g., angle of departure for DL, QCL , etc.
    Notes: definition of beam grouping:
      Beam grouping = for TRP(s) or UE to group multiple Tx and/or Rx beam(s) and/or beam pair(s) into one subset of beams

## Slide 3: Proposal-2
    At least following aspects should be included by feedback signaling report based on RS used for beam management
    Selected Tx beam ID(s)
      Notes: Selected Tx beam ID(s) can be in the form of resource selection indicator
    Channel strength/quality information associated with selected Tx beam(s)
    Beam grouping information for Tx beam resources
      e.g., based on RS (used for beam management) transmitted by TRP, UE reports Tx beam ID(s) in each of M beam groups and/or RSRP/CSI with the best beam in each of the M beam groups (M<= total number of selected Tx beams N)
  NR supports with and without a downlink indication to derive beam-group-related information for assisting UE-side beamforming
    Other information is not precluded