## Slide 1: WF on PRS frequency hopping
Ericsson, Qualcomm,…
R1-1703679
3GPP TSG RAN WG1 Meeting #88
Athens, Greece, 13th – 17th Feb 2017
Agenda item 7.2.3.3

## Slide 2: Background
Frequency hopping may help improve OTDOA positioning performance for BL/CE UEs with reduced receiver bandwidth
In RAN1#87, it was agreed that “If activated, PRS frequency hopping is configured with the following parameters (similar to Rel-13 eMTC FH):
  Number of bands for frequency hopping X: {2, 4}
    The first band is in the center
  The positions of the remaining X-1 bands:
    The starting position of each of X-1 bands is indicated separately: narrowband {0,1,…,max-1}”
In RAN1#87, it was agreed to support multiple PRS occasions in a legacy PRS period

## Slide 3: Proposals
Starting point of PRS frequency hopping
  The first subframe of the first PRS occasion in a legacy PRS period
Supported PRS bandwidth for frequency hopping
  6 PRBs
Frequency hopping interval: select Option 1 or Option 2
  Option 1: {1, 2, 4, 5, 10, 20} subframes
  Option 2: one PRS occasion