## Slide 1: WF on PUCCH design principles
NTT DOCOMO, INC.
3GPP TSG RAN WG1 #88
Athens, Greece, 13th – 17th February 2017
Agenda: 8.1.3.2
R1-1703797

## Slide 2: Background
Following are possible agreements at Tuesday
Possible agreements:
For short duration PUCCH carrying 1 or 2 UCI payload bits, the design of the PUCCH structure shall consider at least the following aspects:
  BLER
  Multiplexing capacity
  PAPR/CM
  Support of frequency diversity
  Impact on emission
  Multiplexing with other channel/other PUCCH format
  Scalability
Continue offline discussion until Tuesday – Zukang (Huawei)

## Slide 3: Background
Design principles of following PUCCH structures to be discussed
  Short-PUCCH in 1-symbol duration with up to 2 UCI bits
  Short-PUCCH in 1-symbol duration with more than 2 UCI bits
  Short-PUCCH in 1-symbol duration with up to 2 UCI bits
  Short-PUCCH in 2-symbol duration with more than 2 UCI bits
  Long-PUCCH with up to 2 UCI bits
  Long-PUCCH with more than 2 UCI bits

## Slide 4: Proposals
For a given UCI payload, short-PUCCH in 1-symbol duration is designed such that:
  UE multiplexing capacity can be less than that of long-PUCCH
  Frequency-diversity gain should able to be similar to long-PUCCH
  Interference randomization should be enabled
  Strive for scalable design with short-PUCCH with more than 2 UCI bits
  PAPR/CM lower than CP-OFDM when/if possible

## Slide 5: Proposals
For a given UCI payload, long-PUCCH is designed such that:
  UE multiplexing capacity should be same/similar to LTE PUCCH
  PAPR/CM should be same/similar to LTE PUCCH
  Frequency-diversity gain should be same/similar to LTE PUCCH
  Interference randomization should be enabled
  Strive for scalable design with long-PUCCH with more than 2 UCI bits