## Slide 1: Way forward on Reduced system acquisition time in NB-IoT
Ericsson,…
3GPP TSG-RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.5
R1-1709216

## Slide 2: Background
In RAN1#88bis meeting, regarding system acquisition time reduction, it was agreed that at least the following candidates can be considered.
  Enhancement(s) to NPSS/NSSS
  Enhancement(s) to MIB-NB
  SIB1-NB accumulation across multiple SIB1-NB TTIs (with or without specification impact)
  New mechanism allowing to skip SIB1-NB and/or SI messages and/or MIB-NB reading
  Additional SIB1-NB is transmitted on other subframes in addition to the existing SIB1-NB transmission
  Use of physical signal/channel in agenda item 7.2.7.1.1 (if introduced). Note: This is the wake-up or go-to-sleep signal being considered.
  FFS on other SIBx-NB
  Details of all solutions are FFS
  Solutions need to be backwards compatible and take care of impacts to Rel-13/Rel-14 networks
It is shown in R1-1706894 that the NPBCH can be combined over several 640 ms TTI, which can significantly improve the performance without increasing the complexity.

## Slide 3: Proposal
Consider advanced MIB decoding schemes as a technique for improving MIB acquisition time.
Propose to RAN4 that new PBCH demodulation requirements based on combination across the 640 ms PBCH TTI are introduced in Rel-15.