## Slide 1
WF on NZP CSI-RS for interference measurement
Huawei, HiSilicon, Xinwei, MediaTek, AT&T, CeWiT, Intel, ZTE, ZTE Microelectronics, IITH, IITM, China Unicom, Tejas Networks, Softbank, Qualcomm, LGE, Ericsson, KDDI, Deutsche Telekom, Mitsubishi Electric, InterDigital, NEC, SONY, Spreadtrum, China Telecom, CATR, SHARP
3GPP TSG RAN WG1 Meeting #89 R1-1709295
Hangzhou, China, 15-19 May 2017
Agenda item: 7.1.2.3.2

## Slide 2: Background
Agreements:
For NR, support at least two types of resources used for interference measurement in CSI configuration based on the following candidates:
  ZP CSI-RS, NZP CSI-RS, DMRS
    Including independent or joint usage of any combination of the above three candidates
  Selection is to be done in RAN1#88
For interference measurement, down selection from options will be conducted.
  NZP CSI-RS based
    Opt. A1: Estimation on NZP CSI-RS for channel estimation (by subtracting CSI-RS from Rx signal)
    Opt. A2: Emulation on NZP CSI-RS which is represented by multiplied value of channel and precoding matrix
  DM-RS based
    Opt. B1: Estimation on DM-RS for own data demodulation (by subtracting DM-RS from Rx signal)
    Opt. B2: Estimation on DM-RS for other UEs

## Slide 3: Proposals
Support at least NZP CSI-RS based interference measurement
  select at least one of following scheme
    Scheme-1: Estimation on NZP CSI-RS for channel estimation (by subtracting CSI-RS from Rx signal)
    Scheme-2: Emulation on NZP CSI-RS which is represented by multiplied value of channel and precoding matrix
  Other schemes are not precluded