## Slide 1: WF on beam indication for PDCCH
Samsung
R1-1709381
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15 – 19 May 2017
Agenda item 7.1.2.2.1

## Slide 2: Background
For reception of unicast DL data channel, support indication of spatial QCL assumption between DL RS antenna port(s) and DMRS antenna port(s) of DL data channel: Information indicating the RS antenna port(s) is indicated via DCI (downlink grants)
  The information indicates the RS antenna port(s) which is QCL-ed with DMRS antenna port(s)
    FFS: Indication details
      E.g. explicit indication of RS port/resource ID, or implicitly derived
  FFS when the indication is applied (e.g., the indication is assumed only for the scheduled PDSCH or until next indication; when the above information is included, if there should be a scheduling/beam switch offset, etc.)
  FFS: Beam indication for receiving fall back unicast PDSCH (if supported)
  Note: related signalling is UE-specific
FFS: Beam indication (if needed) for receiving (UE-group) common PDSCH for RRC connected UE
Candidate signalling methods for beam indication for a NR-PDCCH (i.e. configuration method to monitor NR-PDCCH)
  MAC CE signalling
  RRC signalling
  DCI signalling
  Spec-transparent and/or implicit method
  Combination of the above

## Slide 3: Proposals
For single PDCCH BPL monitoring, the following signaling method for beam indication for a NR-PDCCH (i.e. configuration method to monitor NR-PDCCH) is supported
  RRC signaling
For multiple PDCCH BPLs monitoring, the following signaling method for beam indication for a NR-PDCCH (i.e. configuration method to monitor NR-PDCCH) is supported
  Combination of MAC CE + RRC signaling
  The support of DCI signaling can be further considered