## Slide 1: WF on UE-UE cross-link interference measurement
Huawei, HiSilicon
3GPP TSG RAN WG1 #89 Meeting R1-1709393
Hangzhou, China, 15th – 19th April 2017
Agenda item: 7.1.6.1

## Slide 2: Background
Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Proposal
The following is supported for UE-UE cross link interference measurement and reporting
  UE-UE interference measurement is based on SRS
    A UE may be configured with multiple SRS configurations, e.g. one SRS configuration for UE-UE cross-link interference measurement and another SRS configuration for UL channel sounding
  One or more sets of UE-UE measurement configurations is provided to a UE for UE-UE cross-link interference measurement and reporting
    FFS details on the UE-UE measurement configuration
  The UE-UE measurement report shall include at least
    Metric of the UE-UE interference measurement, e.g. RSRP
    The UE-UE measurement resource (e.g. time/frequency/code) associated with the reported metric