## Slide 1: WF on L1 Comparison of Unidirectional and Bidirectional Relaying
Intel, Huawei, HiSilicon, ITRI
3GPP TSG RAN WG1 Meeting #89 R1-1709406
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item - 6.2.9.2.3.1

## Slide 2: Background
The following conclusion was reached in the previous meeting:
  Continue analysis of unidirectional UL and bidirectional relaying modes and identify commonality from physical layer perspective

## Slide 3: Proposal (1/2)
Capture the following comparison in TR 36.746
L1 Design Aspect | Bidirectional Relaying | Unidirectional Relaying
Synchronization | eRemote UE coverage: In-coverage and partial coverage scenarios. Sync source: eNB or eRelay UE (SLSS) | eRemote UE coverage: In-coverage scenario only Sync source: eNB
Discovery | PSDCH based eRelay discovery is possible | PSDCH based eRelay discovery needs improvement eNB assistance is needed to discover eRelay UE and establish connection.
Relaying operation | DL reception is from eRelay UE UL transmission is through eRelay UE | DL reception is from eNB UL transmission is through eRelay UE
Resource management | eNB and/or eRelay can control eRemote UE TX/RX resources eRemote UE can use autonomous resource allocation mode | Only eNB can control eRemote UE TX/RX resources eRemote UE can use autonomous resource allocation mode

## Slide 4: Proposal (2/2)
L1 Design Aspect | Bidirectional Relaying | Unidirectional Relaying
ACK/NACK Feedback | Uu link: Legacy HARQ operation can be reused for DL and UL transmission with potential enhancements for DL PC5 link: Signaling for RLC-AM status report and/or decoding status needs to be defined. | Uu link: Legacy principle of operation can be reused for UL only. Modifications are needed for DL HARQ support, which do not seem trivial. PC5 link: Signaling for RLC-AM status report and/or decoding status needs to be defined. Sidelink DL RLC AM status report and/or decoding status can be routed through eRelay UE (PSSCH and PUSCH) Sidelink UL RLC AM status report and/or decoding status can be sent directly through PDSCH
Measurements | Both eRelay and eRemote UE can perform sidelink measurements (e.g. PC5 RSRP/RSSI) | eRemote UE cannot perform sidelink measurements.
Sidelink power control | Bidirectional sidelink power control is possible w/o close eNB involvement, i.e. sidelink power control at the eRelay and eRemote UE side. | eRelay UE cannot directly adjust TX power of Type-2 eRemote UEs. eRemote UE sidelink power control can be done through additional eNB signaling.
DL CSI feedback | N/A | DL CSI either needs to be relayed or transmitted directly to eNB or omitted