## Slide 1
3GPP TSG RAN WG1 Meeting RAN1#88bis R1-1709442
Hangzhou, China, 15th – 19th May, 2017
Agenda item: 7.1.1.1.3
WF on Time Index Indication of SS Block
Huawei, HiSilicon, InterDigital, NTT DoCoMo, …

## Slide 2: Background
The following agreements were achieved in RAN1 #88bis,
  On SS burst set periodicity
  SS burst set periodicity default value for initial cell selection: 20/20 msec
    Note that RAN1 assumes that RAN4 will investigate requirements
  Same set of configuration values for SS periodicity for CONNECTED/IDLE & non-standalone cases
  Values for configuration set for CONNECTED/IDLE & non-standalone case
    {5, 10, 20, 40, 80, 160} ms
    FFS: how the at least a part of SFN is indicated in PBCH in relation to PBCH TTI
  On number of SS blocks
  The considered maximum number of SS-blocks, L, within SS burst set for different frequency ranges are
    For frequency range up to 3 GHz, the maximum number of SS-blocks, L, within SS burst set is [1, 2, 4]
    For frequency range from 3GHz to 6 GHz, the maximum number of SS-blocks, L, within SS burst set is [4, 8]
    For frequency range from 6 GHz to 52.6 GHz, the maximum number of SS-blocks, L, within SS burst set is [64]
  The way the value of L is reflected in specification is FFS
    Aforementioned values are to be used to facilitate the NR initial access design and evaluate the specification impact
    Possibility of having unified frequency agnostic signaling design is not precluded

## Slide 3: Background
The following agreements were achieved in RAN1 #88bis,
  PBCH TTI: 80 msec
  Time index indication: PBCH conditioned that mobility and HO related requirements can be met
    Note: RAN1 assumes that RAN2 will check against to RAN2 requirements

## Slide 4: Proposal
For SS block time index indication, the following should be supported
  Combination of explicit and implicit indications by PBCH
    Implicit bits are used for SS block time index indication within SS burst
    Explicit bits are used for SS burst time index within SS burst set