## Slide 1: WF on non-codebook based transmission for UL
NTT DOCOMO, InterDigital, Intel, [Samsung], [ZTE], [LG], [Ericsson] …
R1-1709484
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 7.1.2.1.4

## Slide 2: Background
Agreements:
Support at least the following UL transmission schemes for data in NR
  Scheme A: Codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than X (FFS: Value of X).
    Study codebook design including single-stage and multi-stage, e.g., W1W2 structure, codebook
    Study the following DL signaling, e.g.,
      One level DCI
      Two level DCI
      MAC CE
      DCI associated with PDSCH (like UCI associated with PUSCH in LTE)
  Scheme B: Non-codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than Y (FFS: Value of Y).
    Support the indication of DL measurement RS for UE to calculate candidate precoder
    Study the mechanisms for UL precoder determination, e.g. precoded SRS based, non-precoded SRS based, hybrid precoded and non-precoded SRS based
  Diversity-based transmission schemes
    FFS: Whether the scheme has specification impact or not
FFS: Merging of the schemes

## Slide 3: Proposals
Support UE to use same beam with DL Rx beam for UL non-codebook based transmission
  E.g., when UE holds beam correspondence and gNB allows
  FFS: UE determines UL Tx beam for each sub-band for frequency selective precoding
  One of K CSI-RS resource(s) is selected by gNB is used to determine the UL Tx beam for PUSCH
    K is equal to or lager than 1
    FFS: multiple CSI-RS resources selection
    FFS: semi-static configuration and/or dynamic indication
As long as gNB indicates UL Tx beam, e.g., SRI, UE follows the indication