## Slide 1: WF on Long PUCCH
Qualcomm
[]
3GPP TSG RAN WG1 Meeting #89 R1-1709527
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.3.2.2
Document for decision

## Slide 2: Background
Agreements (88bis):
The set of the number of symbols for long duration NR-PUCCH in a slot includes {4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14}
  FFS whether or not it depends on the slot type, # of symbols per slot, etc.

## Slide 3: Proposal
For long PUCCH, support DMRS at fixed locations with respect to symbol 0 in the slot, regardless of the starting symbol of long PUCCH.
  For 1 or 2 bit(s) UCI payload
    The set of DMRS locations are symbol {1, 3, 5} for 7-symbol slot
    The set of DMRS locations {1, 3, 5, 8, 10, 12} for 14-symbol slot
    Depending on the long PUCCH duration, a subset of the above DMRS locations can be used.