## Slide 1: WF on Sequence design for SRS
Ericsson, Panasonic, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.2.4.4
R1-1709551

## Slide 2: Previous Agreements
Agreement:
To down-select one method for NR SRS sequence generation based on at least the following alternatives:
  Alt-1: SRS sequence is a function of the sounding bandwidth and does not depend on the sounding bandwidth position or the PRB position.
    Sequence design and other design details are FFS.
  Alt-2: SRS sequence is a function of the sounding bandwidth position or the PRB position.
    Sequence design and other design details are FFS.
  Taking into account metrics such as PAPR, capacity/flexibility, etc.
  Other parameters, if any, determining SRS sequence are FFS (e.g. SRS sequence ID)
Agreements:
Scheduling SRS resources to multiple UEs where the resources have full and/or partial overlap of SRS time-frequency resources (REs) is supported, where
  The multiple SRS resources can share the same root sequence values in the overlapping REs to allow for low or zero mutual cross-correlation
  FFS: Minimum overlap granularity to ensure zero cross-correlation
  FFS: Detailed sequence design taking into account

## Slide 3: Proposal
Alt2 is supported:
  For an SRS resource, NR supports SRS sequences that are a function of the sounding bandwidth position or PRB position
FFS: Detailed sequence design taking into account at least Cubic Metric, PAPR, and cross-correlation properties amongst overlapping and partially overlapping SRS resources