## Slide 1: WF on NPRACH Reliability Enhancements Qualcomm, …
3GPP TSG RAN WG1 89 R1-1709635
Hangzhou, China
15 th– 19th May, 2017
Agenda item: 6.2.7.3
Document for decision

## Slide 2: Background
In the WID, the following objective is included
  If found necessary, reduce false alarm probability for NPRACH detection due to inter-cell interference on NPRACH
Inter-cell NPRACH interference occurs when two or more NPRACH resource blocks of neighboring cells overlap and lead to
  Increased NPRACH false alarm probability
  Significantly biased timing estimation: a longer NPRACH transmission interfered by one or more short NPRACH transmissions
Only one out every 5 possible subcarriers are used in current NPRACH
  Up to 5 cells can be FDMed
A cell-dependent rotation of the second or the 4th symbol group allows quick detection of inter-cell NPRACH interference

## Slide 3: Proposal
Adopt the following enhancements for feNB-IoT NPRACH:
  A frequency shift of k*0.75 kHz is applied to all NPRACH signal in a Cell.
    FFS k=[-2, -1, 0, 1, 2] or [-2, -1 1 2].
  A phase rotation of m*p/2 with m=0,1,2,3 is applied to the 4th symbol group of each repetition.
  Signaling of the above frequency shift and phase rotation is FFS.