## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709667
Hangzhou, China, 15th – 17th May 2017
Agenda item: 7.1.2.2.1
WF on UL Beam Management with UE assistance information
MediaTek, Samsung

## Slide 2: Background
Agreements in RAN1 88bis meeting:
  Study whether or not the UE to provide information to gNB to assist UL beam management without UE beam correspondence
    E.g., the amount of SRS resources that is needed to train UE Tx beams, based on DL beam management results if available

## Slide 3: Proposal
  Support UE to provide information to gNB to assist UL beam management
    The information can be a number representing the amount of SRS resources required for UE Tx beam training
    FFS: details
      E.g., a bit string where all-zero bits indicates no Tx beam training is required to determine a beam-correspondent TX beam to a RX beam

## Slide 4: appendix

## Slide 5: Example
Notation
  Ng analog beams per level, Kg levels of beams
  NUE analog beams per level, KUE levels of beams
  Mg: UL Rx beam ambiguity at gNB conditioned on a selected DL gNB Tx beam
  MUE: UL Tx beam ambiguity at UE conditioned on a selected DL UE Rx beam
Hierarchical search type | Ng | NUE | Kg | KUE | Mg | MUE | # beam pair search attempt | Search overhead
Full search | 8 | 4 | 2 | 1 | N/A | N/A | 40 | 100%
Local search | N/A | N/A | N/A | N/A | 3 | 3 | 9 | 22.5%
Full search | 8 | 4 | 2 | 2 | N/A | N/A | 44 | 100%
Local search | N/A | N/A | N/A | N/A | 4 | 4 | 16 | 36%