## Slide 1: WF on UE Processing Time
3GPP TSG RAN WG1 Meeting #89 R1-1709702
Hangzhou,China, 15rd - 19th May 2017
Agenda Item: 7.1.3.3.4
Huawei, HiSilicon, MediaTek, …

## Slide 2: Background
Agreement in RAN1#86bis
  For slot-based scheduling, NR specification should support the following
    DL data reception in slot N and corresponding acknowledgment in slot N+K1
      All UEs should support K1≥1 with exact values for K1 FFS
      Some UEs may support K1=0 (FFS conditions)
    UL assignment in slot N and corresponding uplink data transmission in slot N+K2
      All UEs should support K2≥1 with exact values for K2 FFS
      Some UEs may support K2=0 (FFS conditions)

## Slide 3: Background
Agreements in RAN1 #ad hoc 2007-1
  NR UE supports a set of minimum HARQ processing time
    FFS: set size
  NR supports different minimum HARQ processing time at least for across UEs
    The HARQ processing time at least includes:
      Delay between DL data reception timing to the corresponding HARQ-ACK transmission timing
      Delay between UL grant reception timing to the corresponding UL data transmission timing
    NR UE is required to indicate its capability of minimum HARQ processing time to gNB
      FFS how the capability is indicated by UE
        e.g. reported processing time granularity
        e.g. dependency of DMRS pattern configuration
    FFS definition of minimum HARQ processing time

## Slide 4: Background
The following factors should be considered when defining the minimum value of K1
  The maximum DL TB size
  The maximum DL data rate
  SCS and slot duration
  Channel bandwidth
  RS design, including at least DMRS for NR-PDCCH, DMRS for NR-PDSCH and DM-RS for NR-PUCCH
  Channel coding schemes
  Resource mapping schemes, including NR-PDCCH structure and NR-PDSCH resource mapping schemes
  Transmission delay (TA)
  NR-PUCCH design (long or short)
  Gap duration for DL/UL switching
  The maximal number of aggregated component carriers assumed in CA
The following factors should be considered when defining the minimum value of K2
  The maximum UL TB size
  The maximum UL data rate
  SCS and slot duration
  Channel bandwidth
  RS design, including at least DMRS for NR-PDCCH and DMRS for NR-PUSCH
  Channel coding schemes
  Resource mapping schemes, , including NR-PDCCH structure and NR-PUSCH resource mapping schemes
  Transmission delay (TA)
  Gap duration for DL/UL switching
  The maximal number of aggregated component carriers assumed in CA
To give more flexibility, a relatively larger K1 and K2 should be adopted in Rel-15.

## Slide 5: Proposal
Considering the processing load of NR, it is recommended the typical values in LTE as a starting point for NR, that is,
  K1=4 for SCS 15KHz slot-based scheduling
  K2=4 for SCS 15KHz slot-based scheduling