## Slide 1: WF on SS Block Bandwidth and Minimum Carrier Bandwidth for NR below 6GHz
CMCC,
3GPP TSG RAN WG1 #89 | R1-1709818
Hangzhou, China, May 15 – 19 2017 | Agenda Item: 4

## Slide 2: Background
RAN4 sent a LS (R1-1706872) informing RAN1 of the following agreement:
RAN4#82bis agreement:
The set of supported NR bandwidths for each frequency band will be band specific
For frequency range up to 6 GHz, the minimum possible carrier bandwidth for NR is 5 MHz
For frequency range from 6 GHz to 52.6 GHz, the minimum possible carrier bandwidth for NR is 50 MHz
RAN4 will further determine mapping between frequency band and the set of support carrier bandwidth values in consideration with above

## Slide 3: Background
RAN1#88bis agreement:
Agreements:
Working assumption: Number of PSS sequences: 3
  PSS sequence details:
    Frequency domain-based pure BPSK M sequence (fixing the time/freq. offset ambiguity)
      1 polynomial: octal 145 Decimal 145 (i.e. g(x) = x7 + x4 + 1)
      In freq. domain 3 cyclic shifts (0, 43, 86) to get the 3 PSS signals
      Initial poly shift register value: 1110110
    FFS modified ZC: 2 ZC sequences concatenation or interleaving in time or freq., 4 ZC sequences concatenation in time
Number of SSS signals: 1000 post-scrambling
PSS sequence length: 127 for frequency domain-based pure BPSK M sequence
  Note that PSS will be mapped to consecutive 127 subcarriers
SSS sequence length: 127
Subcarrier spacings for PSS/SSS for difference freq. ranges: 15kHz/30kHz for below 6 GHz, and 120kHz/240kHz for above 6 GHz
  Note: RAN1 assumes that RAN4 will decide it depending on frequency ranges
SSS sequence details: Long M-sequence with scrambling
SYNC frequency raster: RAN1 assumes that RAN4 will decide it
SS burst set periodicity default value for initial cell selection: 20/20 msec
  Note that RAN1 assumes that RAN4 will investigate requirements
Time index indication: PBCH conditioned that mobility and HO related requirements can be met
  Note: RAN1 assumes that RAN2 will check against to RAN2 requirements
PBCH BW: 288 subcarriers, 2 OFDM symbols (additional symbols if MIB size larger than assumed)
PBCH phase reference: DMRS
PBCH TTI: 80 msec

## Slide 4: Discussion
Based on the agreements made in RAN1 (288 subcarriers for PBCH ) and RAN4, SS Blocks using SCS of 30kHz are precluded within bands which only support the minimum bandwidth defined for frequency ranges below 6GHz
However RAN1 has identified benefits for utilizing a larger SCS for the SS Block in below 6GHz:
  More robustness to CFO (especially for high doppler case)
  Lower latency for initial access
  Reduced time-domain overhead
Since the SS Block SCS is mapped to each frequency band in the specification it is critical to address this issue in Rel.15 considering performance and forward compatibility

## Slide 5: Proposal
RAN1 should send a LS to RAN4 informing them that because of the inability of the 5MHz minimum carrier bandwidth to support SS Blocks with 30kHz SCS, RAN1 is requesting that a minimum carrier bandwidth value of 10MHz is supported in addition to 5MHz in order to accommodate SS Blocks with 30kHz SCS for bands, where appropriate in the frequency range below 6 GHz.