## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-171532
Prague, Czech Republic, 21-25 August 2017
Agenda item: 6.1.1.5.3
WF on Radio link monitoring
Huawei, HiSilicon

## Slide 2: Background
Following agreements on RLF and RLM in NR were achieved in RAN1 #NR Adhoc 2:
  Agreements:
    Both CSI-RS based RLM and SS block based RLM are supported
    FFS: whether or not only a single type of RS is configured to UE for RLM at a time
    NR should strive to provide aperiodic indication(s) based on beam failure recovery procedure to assist radio link failure (RLF) procedure, if same RS is used for beam failure recovery and RLM procedures.
    Example 1: aperiodic indication(s) based on beam failure recovery procedure can reset/stop T310
      RAN2 can decide specific procedure
    Example 2: aperiodic indication(s) based on failure of beam recovery procedure
      How to use aperiodic indication can be decided in RAN2
    FFS: aperiodic indication(s) based on beam failure recovery procedure to assist RLF procedure if different RS is used

## Slide 3: Proposal
NR should support UE to send aperiodic indications from success of beam recovery procedure to L3.
  RAN2 can decide specific procedure for RLM, e.g. reset/stop T310.