## Slide 1: Way forward on power sharing for LTE-NR NSA operation
Ericsson, CATT, Nokia, NSB, Samsung, [Mediatek], Huawei
R1-1715090
RAN1 #90
Prague, Czech Republic, 21-25 August 2017
Ag. 6.1.7.1

## Slide 2: Background
Agreements:
Regarding power sharing for LTE-NR dual connectivity, support at least semi-static power sharing between LTE and NR
  FFS details
  Discuss further whether or not to support dynamic power sharing between LTE and NR
  Discuss further impacts due to other factors, e.g., different TTI lengths, channel/service types, synchronous vs. asynchronous, different processing latency for LTE vs. NR, assumption regarding communication between NR vs. LTE at UE, specification impact to LTE (if any) and/or NR, etc.

## Slide 3: Terminology/Background
Terminology
  P_LTE (max allowed LTE power); P_NR (max allowed NR power)
  P_cmax (max allowed UE power), i.e., a limit that is similar to ‘The configured maximum UE output power’ that was specified for LTE.
  P_MeNB (guaranteed power for LTE); P_SeNB (guaranteed power for NR)
Semi-static power sharing (i.e., current agreement for NR)
  UE configured with P_LTE , P_NR (No need for P_MeNB ; P_SeNB )
  Network choice : P_LTE + P_NR = P_cmax (i.e., P_NR = X => P_LTE = P_cmax – X)
  Comment: Maximum transmit power of LTE is reduced when NR is configured. For example, assuming a 23dBm UE, when NR is configured, regardless of presence of simultaneous transmissions, maximum transmit power of UE is reduced to 20dBm to operate NR with up to 20dBm transmit power. (e.g. see R1-1714460, Ericsson)
Dynamic power sharing based on LTE-LTE DC (i.e., PCM2)
  UE configured with P_MeNB ; P_SeNB
  Network choice : P_MeNB + P_MeNB = P_cmax or P_MeNB + P_SeNB > P_cmax or P_MeNB + P_SeNB < P_cmax
    First choice available with semi-static;
  eNB configures P_MeNB + P_SeNB < P_cmax and there is a notion of ‘remaining power’. How ‘remaining power’ is shared, and which transmission the UE should prioritize when total transmit power exceeds P_cmax is specified explicitly (e.g. as LTE power control specifications for dual connectivity)
  Comment: Increases UE implementation complexity. Given the schedule of release 15, it is very difficult to finalize the standardization (e.g. see R1-1713478, Qualcomm)

## Slide 4: PROPOSAL (1)
At least for LTE-NR NSA operation
  Maximum allowed power values for LTE (P_LTE) and NR (P_NR) are set separately
    i.e., when UE is configured for NR, P_LTE can be configured up to P_cmax and P_NR can be configured up to P_cmax.
    e.g. P_LTE + P_NR > P_cmax or P_LTE + P_NR = P_cmax
  Signaling details for P_LTE, P_NR are left to RAN2, RAN4.
  Note: ‘P_cmax’ is a limit that is similar to ‘The configured maximum UE output power’ that was specified for LTE.
  Note: The network will still have flexibility to prioritize or reserve certain NR transmission power depending on network implementation

## Slide 5: Offline discussion status
Options for UE power scaling
  Option 1 (Ericsson, CATT, Samsung)
    If total transmit power exceeds P_cmax,
      For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation;
      For LTE, no change in power control procedure
  Option 2 (Ericsson, CATT, Samsung, [Mediatek])
    At least, when DL/UL LTE sTTI/reduced UE processing time based operation is not configured for the UE, if total transmit power exceeds P_cmax,
      For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation;
      For LTE, no change in power control procedure
  Option 3 (Nokia,NSB)
    For LTE-NR DC, where eNB is master, support 3 RRC configured power sharing-modes (NPL, LTE-PL, NR-PL), where P_LTE to MCG and P_NR to SCG
      Master eNB indicates to a UE the selected mode using MAC-CE
      Details in R1-1714097
  Option 4 (Huawei)
    Dynamic power sharing is supported such that the remaining power of CG1 (e.g, LTE CG) from its guaranteed power can be utilized by CG2 (e.g., NR CG) when the UE is aware of the transmission power of CG1.
    Power allocation priority for remaining power of LTE-NR DC is determined by the earlier transmission of scheduling information.
  Option 5 (…)