## Slide 1: WF on UE GNSS Carrier Phase Measurement
Nokia, Nokia Shanghai Bell, Qualcomm, Ericsson, Huawei, HiSilicon
R1-1715096
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017
Agenda Item: 5.2.10

## Slide 2: Background
A new Study Item on “UE positioning accuracy enhancements for LTE” was approved in RAN#75 meeting with one of objectives to support Real-Time Kinematic (RTK) GNSS in LTE.
UE needs to report code-phase measurement and carrier-phase measurement of GNSS satellite signals to E-SMLC for UE-assisted/network-based RTK GNSS positioning in LTE network.
LTE already supports the report of code-phase measurement and carrier-phase measurement from UE to E-SMLC for RTK GNSS positioning.
UE GNSS code measurement has been defined in TS 36.214 but UE GNSS carrier-phase measurement is not.

## Slide 3: Proposal
Proposal: Define UE GNSS carrier-phase measurement in TS 36.214.
Definition | The number of carrier-phase cycles (integer and fractional parts) of the ith GNSS satellite signal, measured since locking onto the signal. Also called Accumulated Delta Range (ADR). The reference point for the GNSS carrier phase shall be the antenna connector of the UE.
Applicable for | Void (this measurement is not related to E-UTRAN/UTRAN/GSM signals; its applicability is therefore independent of the UE RRC state)