## Slide 1: WF on Reduced PMI Payload in Type II Codebook
Nokia, Nokia Shanghai Bell, Samsung, Ericsson, [Docomo]
3GPP TSG-RAN WG1#90 R1-1715216
Prague, Czech Republic, 21st – 25th August 2017
Agenda: 6.1.2.2.3

## Slide 2: Background
The Type II NR codebook was agreed at RAN1#89 as described in R1‑1709232
The agreement includes the following in reference to the wideband (WB) amplitude feedback:
  PMI payload can vary depending on whether an amplitude is zero or not
    Details are FFS
This WF proposes the details for achieving the reduced payload, where the payload reduction occurs in the feedback of subband (SB) differential amplitude and subband phase.

## Slide 3: Proposal
For beams where the reported wideband amplitude is zero, the corresponding subband amplitude (if configured) and phase coefficients are not reported, with details defined on the next two slides.

## Slide 4: Detail: definitions
Let () be the wideband amplitude coefficient indicators for layer , where is the RI.
Let the strongest coefficient on layer be identified by ()
Let and () be the subband phase coefficient indicators and the subband amplitude coefficient indicators for layer , respectively, where is the RI.
is the configured PSK constellation size used for SB phase reporting (4 or 8).
is the number of full resolution subband coefficients when WB+SB amplitude is configured.
[TypeIIAmplitude] is the higher layer parameter used to configure the amplitude feedback of the Type II codebook. It may be set to [WBAmplitude] for WB-only amplitude feedback or to [WB+SBAmplitude] for WB amplitude feedback with differential SB amplitude feedback.

## Slide 5: Detail: specification
The reporting procedure for the amplitude and phase coefficients is modified as follows to include payload reduction for the subband indicators (changes in red). The proposal applies to both the Type II codebook and the Type II codebook extension for beamformed CSI-RS.
  The indicators , , and (). , , and are not reported for .
  The remaining elements of () are reported, where . Let () be the number of elements of that satisfy
  The remaining elements of and () are reported as follows:
    When [TypeIIAmplitude] is set to [WBAmplitude],
      for , and . is not reported for .
      For , the elements of corresponding to the coefficients that satisfy , as determined by the reported elements of , are reported, where and the remaining elements of are not reported and are set to .
    When [TypeIIAmplitude] is set to [WB+SBAmplitude],
      For , the elements of and corresponding to the strongest coefficients (excluding the strongest coefficient indicated by ), as determined by the corresponding reported elements of , are reported, where and . The values of are given in Table 5.2.1.2-21. The remaining elements of are not reported and are set to . The elements of corresponding to the next weakest non-zero coefficients (excluding the strongest coefficient indicated by ) are reported, where . The remaining elements of are not reported and are set to .
      When two elements, and of the reported elements of are identical (), then element is prioritized to be included in the set of the strongest coefficients for and () reporting.