## Slide 1: Discussion on DL LBRM Code Rate
MediaTek
R1-1719062
3GPP TSG RAN WG1 Meeting #90-Bis
Prague, Czech Republic, 9th - 13th Oct. 2017
Agenda item 7.3.3.5

## Slide 2: Background
Agreement for NR soft buffer:
Another code rate target that can provide both T-put and performance advantages over LTE is identified as follows.

## Slide 3: Observation (1)
LDPC is selected over Turbo for significant T-put advantage at peak code rate
Evident T-put advantage for code rate >= 2/3

## Slide 4: Observation (2)
LTE RLBRM LTE is around 2/3 across UE categories
NR LDPC performance is better than LTE Turbo.
Setting RLBRM = 2/3 for NR can provide both evident T-put and performance advantages over LTE.
DL UE Category | Max. TBS (bits) | Limited buffer size (bits) | RLBRM
Cat-4 | 75376 | 114192 | 0.66
Cat-6 | 75376 | 114192 | 0.66
Cat-10 | 75376 | 114192 | 0.66
Cat-12 | 97896 | 152256 | 0.64
Cat-15 | 100752 | 152256 | 0.66
Cat-16 | 100752 | 159868 | 0.63

## Slide 5: Conclusion
For DL LBRM, code rate RLBRM = 2/3 is suggested for the evident T-put and performance advantages over LTE.