## Slide 1: WF on observations for RSRP statistics in interference detection
NTT DOCOMO, Nokia, Nokia Shanghai Bell
3GPP TSG RAN WG1 Meeting 90bis R1-17xxxxx
Prague, CZ, 9th – 13th, October 2017
Agenda Item: 6.2.7.4

## Slide 2: Proposal
Capture RSRP statistics results in Appendix and observations for interference detection analysis into the TR
Send LS to RAN2 to inform RSRP statistics results and observations for interference detection analysis

## Slide 3: Proposal
RAN1 observes followings based on RSRP statistics
  Aerial UEs have higher probability of having more strong interfering TPs than terrestrial UEs, and have lower probability of having zero or fewer strong interfering TPs than terrestrial UEs.
  Note: For 2D distance based RSRP statistics [1-4], RSRP gap is RSRP of serving cell minus RSRP of n-th strongest neighbour cell. For uniform UE distribution based RSRP statistics [5-8], RSRP gap is RSRP of n-th strongest neighbour cell minus RSRP of serving cell.
  Note: RSRP measurement error is not modelled in the simulation

## Slide 4: Proposal (cont.)
Observation in UMa AV
  2D distance based RSRP statistics
    Source 1, 2, 3, 4 shows that RSRP gap within [6] dB is observed in 0-[2] neighbour cells when UE height is 1.5 m
    Source 1 shows that RSRP gap within [6] dB is observed in 0-[9] neighbour cells when UE height is above or equal to [100] m
    Source 2 shows that RSRP gap within [6] dB is observed in 0-[9] neighbour cells when UE height is above or equal to [100] m
    Source 3 shows that RSRP gap within [6] dB is observed in 0-[7] neighbour cells when UE height is above or equal to [100] m
    Source 4 shows that RSRP gap within [6] dB is observed in 0-[9] neighbour cells when UE height is above or equal to [100] m
    Source 1, 2, 4 shows that number of neighbour cells within [6] dB RSRP gap is smaller when UE is located closer to serving cell in terms of 2D distance and UE height is above or equal to [100] m
    Note: Above observation is made based on averaged RSRP gap of all UEs which has same 2D distance and height assuming 2D distance based RSRP statistics

## Slide 5: Proposal (cont.)
Observation in UMa AV
  Uniform UE distribution based RSRP statistics
    Source 5 shows that RSRP gap within -6dB is observed in
      0-6 neighbour cells for terrestrial UE percentages of 68.8%, 23.3%, 6.5%, 1.1%, 0.2%, 0.04% and 0.005% at height of 1.5m respectively.
      0-11 neighbour cells for aerial UE percentages of 16.7%, 19.0%, 18.4%, 15.9%, 12.0%, 8.2%, 4.9%, 2.7%, 1.2%, 0.6%, 0.2% and 0.1% at height of 50m respectively.
      0-13 neighbour cells for aerial UE percentages of 17.9%, 15.1%, 13.2%, 11.7%, 10.7%, 9.5%, 7.7%, 5.9%, 4.0%, 2.4%, 1.1%, 0.4%, 0.2% and 0.1% at height of 100m respectively.
      0-14 neighbour cells for aerial UE percentages of 3.2%, 7.1%, 9.4%, 12.9%, 14.6%, 15.0%, 12.6%, 10.8%, 7.8%, 4.6%, 1.4%, 0.4%, 0.1%, 0.1% and 0.1% at height of 200m respectively.
      0-12 neighbor cells for aerial UE percentages of 0.9%, 6.9%, 10.2%, 14.1%, 13.0%, 12.4%, 12.5%, 10.2%, 7.1%, 7.0%, 5.1%, 0.7% and 0.1% at height of 300m respectively.

## Slide 6: Proposal (cont.)
Observation in UMi AV
  2D distance based RSRP statistics
    Source 1, 2, 3, 4 shows that RSRP gap within [6] dB is observed in 0-[2] neighbour cells when UE height is 1.5 m
    Source 1 shows that RSRP gap within [6] dB is observed in 0-[3] neighbour cells when UE height is above or equal to 100 m
    Source 2 shows that RSRP gap within [6] dB is observed in 0-[5] neighbour cells when UE height is above or equal to 100 m
    Source 3 shows that RSRP gap within [6] dB is observed in 0-[7] neighbour cells when UE height is above or equal to 100 m
    Note: Above observation is made based on RSRP statistics averaged over multiple UEs which has same 2D distance and height assuming 2D distance based RSRP statistics

## Slide 7: Proposal (cont.)
Observation in UMi AV
  Uniform UE distribution based RSRP statistics
    Source 5 shows that RSRP gap within -6dB is observed in
      0-8 neighbour cells for terrestrial UE percentages of 60.1%, 23.2%, 9.2%, 4.1%, 1.9%, 0.8%, 0.4%, 0.2% and 0.1% at height of 1.5m respectively.
      0-9 neighbour cells for aerial UE percentages of 21.8%, 19.3%, 19.2%, 15.9%, 11.3%, 7.0%, 3.4%, 1.3%, 0.5% and 0.1% at height of 50m respectively.
      0-10 neighbour cells for aerial UE percentages of 16.9%, 16.9%, 14.8%, 15.9%, 13.6%, 10.3%, 5.9%, 3.6%, 1.3%, 0.4% and 0.2% at height of 100m respectively.
      0-13 neighbour cells for aerial UE percentages of 16.6%, 17.9%, 14.0%, 12.3%, 11.8%, 10.8%, 7.8%, 4.5%, 2.2%, 0.9%, 0.6%, 0.3%, 0.1% and 0.1% at height of 200m respectively.
      0-13 neighbor cells for aerial UE percentages of 17.3%, 16.8%, 17.4%, 15.4%, 12.2%, 8.9%, 5.2%, 3.2%, 1.6%, 1.1%, 0.4%, 0.3%, 0.1% and 0.1% at height of 300m respectively.

## Slide 8: Proposal (cont.)
Observation in RMa AV
  2D distance based RSRP statistics
    Source 1, 2, 3, 4 shows that RSRP gap within [6] dB is not observed when UE height is 1.5 m
    Source 1 shows that RSRP gap within [6] dB is observed in 0-[9] neighbour cells when UE height is above or equal to 100 m
    Source 2 shows that RSRP gap within [6] dB is observed in 0-[9] neighbour cells when UE height is above or equal to 100 m
    Source 3 shows that RSRP gap within [6] dB is observed in 0-[7] neighbour cells when UE height is above or equal to 100 m
    Note: Above observation is made based on RSRP statistics averaged over multiple UEs which has same 2D distance and height assuming 2D distance based RSRP statistics

## Slide 9: References
Source 1 (Huawei) | R1-1716964 | 2D distance based statistics | UMa AV, UMi AV, RMa AV
Source 2 (Ericsson) | R1-1717873 | 2D distance based statistics | UMa AV, UMi AV, RMa AV
Source 3 (ZTE) | R1-1718021 | 2D distance based statistics | UMa AV, UMi AV, RMa AV
Source 4 (NTT DOCOMO) | R1-1718175 | 2D distance based statistics | UMa AV only
Source 5 (Nokia, Nokia Shanghai Bell) | R1-1716990, R1-1718905, R1-1718762 | Uniform UE distribution based statistics | UMa AV, UMi AV

## Slide 10: Appendix
Definition of RSRP statistics based on 2D distance
  Only aerial UEs are evaluated
  UE location:
    Fixed 2D distance and UE height are assumed
      Fixed 2D distances are 0.25*(2/3)*ISD, 0.5*(2/3)*ISD, 0.75*(2/3)*ISD, (2/3)*ISD.
        For 0.25*(2/3)*ISD and 0.5*(2/3)*ISD, all UEs are considered
        For 0.75*(2/3)*ISD, UEs dropped on the arc marked by blue stars are considered
        For (2/3)*ISD, UEs dropped in the area marked by green stars are considered
      Fixed UE heights are 1.5, 50, 100, 200, 300 m
  Small scale fading is not modeled
  RSRP gap between serving cell and n-th strongest neighbor cell is observed
    n = 1, 3, 5, 7, 9

## Slide 11: Appendix
Definition of RSRP statistics based on uniform UE distribution
  UE height: fixed height of {1.5m, 50m, 100m, 200m, 300}
  UE distribution (horizontal): uniform distribution
  Small scale fading is not modeled
  RSRP gap between serving cell and n-th strongest neighbor cell is observed
    n = 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16

## Slide 12: 2D Distance based RSRP Statistics (UMa AV)
 |  | Source 1 |  |  |  | Source 2 |  |  |  | Source 3 |  |  |  | Source 4 |  |  | 
 | UE heights\d_2D | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD
RSRP Serving | 1.5 |  |  |  |  | -34.083 | -42.318 | -50.921 | -47.513 | -35.33 | -43.67 | -51.17 | -47.86 | -34.22 | -42.77 | -49.69 | -48.53
 | 50 |  |  |  |  | -41.451 | -40.758 | -40.146 | -40.516 | -41.51 | -40.43 | -40.1 | -40.73 | -40.66 | -40.48 | -39.93 | -39.84
 | 100 |  |  |  |  | -41.429 | -44.799 | -46.82 | -44.81 | -41.45 | -44.77 | -46.59 | -44.6 | -41.61 | -43.58 | -46.42 | -43.53
 | 200 |  |  |  |  | -50.634 | -49.916 | -50.429 | -50.469 | -50.52 | -50.03 | -50.65 | -50.46 | -49.24 | -50.39 | -50.5 | -52.01
 | 300 |  |  |  |  | -53.201 | -51.289 | -52.82 | -52.167 | -53.21 | -51.4 | -52.9 | -52.18 | -51.68 | -51.87 | -53.76 | -55.44
n=1 | 1.5 | 16.72 | 13.76 | 9.22 | 2.04 | 16.746 | 13.672 | 7.218 | 10.006 | 17.58 | 10.74 | 5.29 | 7.75 | 17 | 13.8 | 9.31 | 1.97
 | 50 | 2.94 | 3.16 | 2.67 | 3.57 | 2.1201 | 2.7002 | 2.5342 | 2.5907 | 7.47 | 2.26 | 2.71 | 2.9 | 2.89 | 3.11 | 2.74 | 3.56
 | 100 | 6.48 | 3.76 | 2.32 | 4.96 | 6.601 | 2.1282 | 2.0807 | 2.2218 | 7.78 | 2.96 | 1.95 | 2.99 | 6.2 | 3.74 | 2.17 | 4.98
 | 200 | 3.35 | 1.55 | 1.05 | 1.1 | 0.93483 | 1.9104 | 2.0276 | 1.905 | 4.4 | 4.47 | 1.68 | 3.17 | 3.3 | 1.58 | 1.06 | 1.07
 | 300 | 2.74 | 2.25 | 0.96 | 0.54 | 0.94713 | 2.9055 | 1.7111 | 2.6048 | 2.05 | 2.26 | 0.48 | 1.44 | 2.77 | 2.24 | 0.96 | 0.57
n=3 | 1.5 | 32.74 | 25.31 | 19.37 | 18.57 | 33.997 | 26.16 | 19.651 | 22.391 | 34.39 | 19.22 | 10.87 | 14.31 | 32.96 | 25.38 | 19.61 | 18.59
 | 50 | 6.67 | 6.41 | 5.8 | 6.89 | 4.8672 | 6.0798 | 6.1077 | 6.1635 | 10.91 | 5.38 | 6.19 | 6.48 | 6.59 | 6.42 | 5.86 | 6.86
 | 100 | 9.1 | 6.67 | 4.71 | 7.34 | 9.0186 | 5.0338 | 4.4639 | 5.3365 | 11.13 | 6.17 | 4.02 | 5.81 | 8.7 | 6.53 | 4.4 | 7.27
 | 200 | 5.11 | 3.45 | 2.47 | 2.4 | 2.5209 | 4.1559 | 3.4485 | 3.7535 | 5.54 | 7.23 | 5.03 | 6.84 | 5.08 | 3.47 | 2.48 | 2.37
 | 300 | 6.46 | 4.12 | 2.38 | 1.22 | 4.5358 | 5.2852 | 3.8628 | 4.4024 | 2.8 | 5 | 6.49 | 6.44 | 6.47 | 4.11 | 2.34 | 1.22
n=5 | 1.5 | 40.86 | 32.17 | 27.19 | 27.05 | 41.212 | 33.423 | 26.217 | 29.12 | 42.37 | 23.29 | 14.41 | 18.5 | 41.26 | 32.25 | 27.48 | 27
 | 50 | 8.82 | 8.63 | 8.14 | 9.29 | 7.0766 | 8.3575 | 8.601 | 8.5684 | 13.13 | 8.34 | 8.92 | 9.47 | 8.68 | 8.61 | 8.23 | 9.36
 | 100 | 10.77 | 8.31 | 6.43 | 8.79 | 10.406 | 6.7434 | 5.8567 | 6.9744 | 13.16 | 9 | 5.77 | 7.93 | 10.22 | 8.04 | 5.95 | 8.62
 | 200 | 6.32 | 4.81 | 4.91 | 3.69 | 4.351 | 5.7931 | 4.332 | 5.0083 | 6.69 | 8.49 | 7.2 | 8.27 | 6.28 | 4.8 | 4.9 | 3.66
 | 300 | 8.58 | 6.24 | 3.47 | 1.78 | 6.7443 | 7.1509 | 4.7909 | 5.911 | 4.4 | 6.73 | 8.29 | 8.03 | 8.58 | 6.19 | 3.44 | 1.78
n=7 | 1.5 | 45.89 | 37.75 | 32.08 | 32.85 | 46.686 | 38.859 | 30.487 | 33.844 | 46.75 | 26.88 | 17.1 | 21.55 | 46.22 | 37.75 | 32.46 | 32.72
 | 50 | 10.43 | 10.52 | 10.27 | 11.42 | 9.1045 | 10.249 | 10.51 | 10.449 | 15.03 | 11.44 | 11.65 | 12.45 | 10.31 | 10.49 | 10.37 | 11.48
 | 100 | 12.36 | 9.76 | 8.14 | 10.01 | 11.606 | 8.138 | 7.0864 | 8.3015 | 16.72 | 11.24 | 7.65 | 9.67 | 11.56 | 9.34 | 7.42 | 9.76
 | 200 | 7.47 | 6.43 | 6.91 | 6.17 | 6.44 | 7.2098 | 5.2913 | 6.8398 | 7.63 | 9.89 | 9.06 | 9.68 | 7.42 | 6.42 | 6.88 | 6.02
 | 300 | 10.26 | 8.44 | 4.81 | 2.46 | 8.1798 | 8.0856 | 6.0617 | 7.1046 | 5.48 | 8.01 | 11 | 9.11 | 10.26 | 8.37 | 4.79 | 2.45
n=9 | 1.5 | 50.31 | 42.51 | 35.63 | 37.37 | 52.162 | 43.139 | 34.046 | 37.745 | 49.88 | 29.74 | 19.5 | 24.01 | 50.75 | 42.52 | 36.08 | 37.25
 | 50 | 11.9 | 12.3 | 12.35 | 13.46 | 11.078 | 11.959 | 12.135 | 12.181 | 16.63 | 14.39 | 14.32 | 15.13 | 11.83 | 12.26 | 12.43 | 13.6
 | 100 | 14.24 | 11.25 | 9.82 | 11.21 | 12.898 | 9.4591 | 8.2638 | 9.5322 | 19.79 | 12.69 | 9.64 | 11.41 | 13.01 | 10.64 | 8.97 | 10.89
 | 200 | 8.54 | 8.57 | 8.51 | 7.39 | 8.5695 | 8.9633 | 9.0556 | 9.1553 | 8.42 | 10.98 | 10.24 | 10.83 | 8.51 | 8.59 | 8.49 | 7.31
 | 300 | 12.38 | 10.02 | 5.92 | 3.59 | 10.507 | 9.8114 | 7.544 | 8.9139 | 7.24 | 9 | 11.95 | 10.15 | 12.39 | 9.95 | 5.87 | 3.44

## Slide 13: 2D Distance based RSRP Statistics (UMi AV)
 |  | Source 1 |  |  |  | Source 2 |  |  |  | Source 3 |  |  |  |  |  |  | 
 | UE heights\d_2D | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD
RSRP Serving | 1.5 |  |  |  |  | -19.91 | -41.604 | -54.098 | -47.562 | -20.21 | -40.99 | -54.3 | -47.69 |  |  |  | 
 | 50 |  |  |  |  | -39.208 | -45.43 | -45.678 | -43.962 | -39.06 | -45.53 | -45.62 | -43.9 |  |  |  | 
 | 100 |  |  |  |  | -41.187 | -46.78 | -48.347 | -47.591 | -41.19 | -46.84 | -48.52 | -47.53 |  |  |  | 
 | 200 |  |  |  |  | -48.512 | -47.417 | -50.718 | -48.839 | -49.03 | -47.61 | -51.46 | -49.53 |  |  |  | 
 | 300 |  |  |  |  | -52.335 | -50.671 | -49.532 | -50.14 | -53.3 | -51.35 | -50.62 | -51 |  |  |  | 
n=1 | 1.5 | 6.81 | 0.05 | 23.54 | 2.15 | 18.092 | 10.247 | 5.6913 | 7.8346 | 16.67 | 12.54 | 7.29 | 9.38 |  |  |  | 
 | 50 | 3.69 | 1.4 | 8.3 | 3.84 | 8.7938 | 2.3781 | 2.8701 | 2.7967 | 2.22 | 3.05 | 2.41 | 2.54 |  |  |  | 
 | 100 | 3.23 | 2.25 | 3.05 | 2.63 | 7.5433 | 3.1996 | 2.2345 | 3.108 | 6.55 | 2.06 | 2.19 | 2.26 |  |  |  | 
 | 200 | 3.6 | 2.75 | 5.38 | 2.43 | 3.8423 | 3.962 | 2.2004 | 3.4627 | 1.12 | 1.82 | 1.89 | 1.92 |  |  |  | 
 | 300 | 3.9 | 2.7 | 3.8 | 3.16 | 2.0507 | 2.4459 | 1.7709 | 2.0836 | 0.96 | 2.85 | 1.72 | 2.63 |  |  |  | 
n=3 | 1.5 | 13.58 | 27.51 | 30.52 | 13.36 | 34.861 | 18.841 | 11.339 | 14.819 | 31.54 | 24.78 | 19.15 | 22.05 |  |  |  | 
 | 50 | 7.54 | 5.75 | 13.54 | 8.28 | 12.929 | 5.9106 | 6.566 | 6.6521 | 4.83 | 6.34 | 6.2 | 6.14 |  |  |  | 
 | 100 | 6.72 | 6.24 | 7.02 | 5.29 | 11.444 | 7.0625 | 4.7171 | 6.4192 | 8.91 | 5 | 4.71 | 5.53 |  |  |  | 
 | 200 | 7.22 | 5.47 | 9.19 | 5.15 | 5.9311 | 6.9963 | 5.7437 | 7.1239 | 2.68 | 4.08 | 3.34 | 3.76 |  |  |  | 
 | 300 | 7.44 | 5.63 | 7.47 | 6.68 | 3.9275 | 5.354 | 7.1032 | 6.5495 | 4.56 | 5.24 | 3.76 | 4.38 |  |  |  | 
n=5 | 1.5 | 17.49 | 35.51 | 36.34 | 18.39 | 42.895 | 23.242 | 14.954 | 18.855 | 39.34 | 31.89 | 25.4 | 28.26 |  |  |  | 
 | 50 | 10.37 | 9.02 | 16.34 | 11.27 | 15.888 | 9.2575 | 9.4288 | 9.9312 | 6.92 | 8.54 | 8.73 | 8.46 |  |  |  | 
 | 100 | 9.28 | 9.64 | 10.97 | 7.15 | 13.797 | 10.261 | 6.9053 | 8.8754 | 10.38 | 6.82 | 6.08 | 7.29 |  |  |  | 
 | 200 | 9.63 | 7.29 | 11.27 | 7.11 | 7.2295 | 8.7944 | 7.9206 | 9.0268 | 4.57 | 5.72 | 4.22 | 4.97 |  |  |  | 
 | 300 | 9.73 | 7.6 | 9.8 | 9.09 | 5.4548 | 7.2192 | 9.5 | 8.473 | 6.71 | 7.05 | 4.69 | 5.84 |  |  |  | 
n=7 | 1.5 | 20.4 | 39.81 | 40.21 | 21.96 | 46.887 | 26.473 | 17.622 | 21.826 | 44.73 | 37.1 | 30.17 | 33.15 |  |  |  | 
 | 50 | 12.98 | 11.64 | 18.46 | 13.7 | 18.356 | 12.522 | 12.291 | 13.092 | 8.89 | 10.71 | 10.61 | 10.31 |  |  |  | 
 | 100 | 11.53 | 12.27 | 15.24 | 8.81 | 18.286 | 12.604 | 9.3628 | 11.225 | 11.6 | 8.13 | 7.28 | 8.55 |  |  |  | 
 | 200 | 11.62 | 8.83 | 12.91 | 8.9 | 8.3612 | 10.282 | 9.8749 | 10.523 | 6.65 | 7.1 | 5.15 | 6.69 |  |  |  | 
 | 300 | 11.55 | 9.15 | 11.67 | 11.07 | 6.9154 | 8.6648 | 11.585 | 9.8756 | 8.16 | 8.01 | 5.87 | 7.03 |  |  |  | 
n=9 | 1.5 | 22.79 | 42.95 | 43.12 | 24.76 | 49.98 | 29.173 | 19.821 | 24.263 | 50.08 | 41.54 | 33.87 | 37.2 |  |  |  | 
 | 50 | 15.5 | 13.88 | 20.29 | 16.03 | 20.705 | 15.558 | 15.151 | 15.933 | 11.1 | 12.59 | 12.18 | 12.01 |  |  |  | 
 | 100 | 13.66 | 14.6 | 17.96 | 10.5 | 21.445 | 14.778 | 12.034 | 13.935 | 12.9 | 9.38 | 8.45 | 9.75 |  |  |  | 
 | 200 | 13.49 | 10.31 | 14.38 | 10.67 | 9.5715 | 11.659 | 11.713 | 11.862 | 8.74 | 8.83 | 8.86 | 9.11 |  |  |  | 
 | 300 | 13.19 | 10.57 | 13.41 | 12.96 | 8.2994 | 9.968 | 12.886 | 11.143 | 10.4 | 9.74 | 7.39 | 8.86 |  |  |  | 

## Slide 14: 2D Distance based RSRP Statistics (RMa AV)
 |  | Source 1 |  |  |  | Source 2 |  |  |  | Source 3 |  |  |  |  |  |  | 
 | UE heights\d_2D | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD | 0.25* (2/3)*ISD | 0.5*(2/3)*ISD | 0.75*(2/3)*ISD | 1.0*(2/3)*ISD
RSRP Serving | 1.5 |  |  |  |  | -23.402 | -34.605 | -37.999 | -36.617 | -25.19 | -34.89 | -39.04 | -37.44 |  |  |  | 
 | 50 |  |  |  |  | -41.188 | -39 | -38.98 | -39.044 | -41 | -39.02 | -39.17 | -38.91 |  |  |  | 
 | 100 |  |  |  |  | -45.984 | -38.772 | -45.036 | -41.807 | -45.89 | -38.96 | -45.23 | -42.25 |  |  |  | 
 | 200 |  |  |  |  | -44.094 | -41.612 | -43.371 | -42.812 | -44.05 | -41.75 | -43.55 | -43.05 |  |  |  | 
 | 300 |  |  |  |  | -46.625 | -44.708 | -44.243 | -45.365 | -46.55 | -44.72 | -44.2 | -45.39 |  |  |  | 
n=1 | 1.5 | 15.75 | 16.93 | 16.72 | 15.46 | 16.609 | 11.211 | 8.7695 | 9.5006 | 14.71 | 10.42 | 8.66 | 9.35 |  |  |  | 
 | 50 | 10.31 | 9.05 | 2.34 | 2.42 | 1.9169 | 2.4948 | 2.3426 | 2.4171 | 1.96 | 2.43 | 2.23 | 2.58 |  |  |  | 
 | 100 | 12.57 | 1.47 | 9.21 | 2.92 | 1.9907 | 8.1374 | 2.1142 | 5.5008 | 2.12 | 7.79 | 1.88 | 5.21 |  |  |  | 
 | 200 | 3.91 | 1.82 | 2.24 | 3.56 | 1.3277 | 1.8612 | 3.9497 | 1.7087 | 1.31 | 1.85 | 3.69 | 1.71 |  |  |  | 
 | 300 | 0.89 | 1.07 | 1.79 | 1.9 | 1.0071 | 1.9993 | 1.2747 | 1.2484 | 1.1 | 2.02 | 1.21 | 1.32 |  |  |  | 
n=3 | 1.5 | 26.85 | 29.92 | 30.11 | 27.65 | 28.836 | 22.076 | 19.527 | 20.36 | 28.5 | 21.53 | 19.67 | 19.76 |  |  |  | 
 | 50 | 14.59 | 13.14 | 5.16 | 5.17 | 4.0679 | 5.4567 | 5.5519 | 5.4628 | 4.26 | 5.37 | 5.27 | 5.72 |  |  |  | 
 | 100 | 15.88 | 3.14 | 11.78 | 5 | 3.9823 | 10.68 | 4.2186 | 7.7027 | 4.03 | 10.32 | 3.99 | 7.21 |  |  |  | 
 | 200 | 6.83 | 5.32 | 6.1 | 8.64 | 4.05 | 7.7492 | 9.0284 | 8.1592 | 4.22 | 7.63 | 8.61 | 7.87 |  |  |  | 
 | 300 | 3.96 | 6.45 | 4.65 | 5.65 | 2.5731 | 4.2433 | 4.2742 | 4.2645 | 2.59 | 4.29 | 4.52 | 4.39 |  |  |  | 
n=5 | 1.5 | 34.53 | 38.84 | 39.23 | 36.04 | 38.33 | 28.598 | 25.376 | 26.513 | 37.49 | 27.75 | 24.87 | 25.65 |  |  |  | 
 | 50 | 17.03 | 15.51 | 7.05 | 6.95 | 5.6537 | 7.4008 | 7.651 | 7.4773 | 5.83 | 7.36 | 7.3 | 7.75 |  |  |  | 
 | 100 | 17.3 | 4.41 | 13.22 | 6.38 | 5.3329 | 12.177 | 5.6233 | 9.1185 | 5.44 | 11.83 | 5.45 | 8.67 |  |  |  | 
 | 200 | 13.65 | 10.85 | 10.64 | 12.19 | 6.7695 | 11.63 | 10.964 | 11.695 | 6.88 | 11.32 | 10.72 | 11.42 |  |  |  | 
 | 300 | 7.81 | 7.71 | 8.1 | 7.71 | 4.1303 | 6.49 | 6.4656 | 6.1658 | 4.21 | 6.47 | 6.6 | 6.29 |  |  |  | 
n=7 | 1.5 | 40.05 | 44.48 | 44.83 | 41.43 | 43.708 | 33.327 | 29.764 | 31.107 | 42.41 | 32.61 | 29.09 | 30.43 |  |  |  | 
 | 50 | 18.74 | 17.19 | 8.52 | 8.36 | 7.0823 | 8.9591 | 9.3116 | 9.0698 | 7.25 | 8.96 | 8.91 | 9.28 |  |  |  | 
 | 100 | 18.46 | 5.62 | 14.46 | 7.63 | 6.4939 | 13.423 | 6.9132 | 10.383 | 6.64 | 13.1 | 6.72 | 10.01 |  |  |  | 
 | 200 | 15.1 | 13.23 | 14.03 | 16.63 | 15.993 | 15.223 | 14.657 | 14.619 | 15.77 | 14.96 | 14.43 | 14.34 |  |  |  | 
 | 300 | 8.59 | 8.51 | 9.2 | 8.9 | 5.5782 | 8.2588 | 7.8857 | 7.6336 | 5.69 | 8.22 | 7.99 | 7.67 |  |  |  | 
n=9 | 1.5 | 43.82 | 48.26 | 48.58 | 45.13 | 47.39 | 36.928 | 33.274 | 34.632 | 45.91 | 36.37 | 32.52 | 33.59 |  |  |  | 
 | 50 | 20.13 | 18.58 | 9.85 | 9.66 | 8.5379 | 10.378 | 10.759 | 10.496 | 8.77 | 10.39 | 10.41 | 10.5 |  |  |  | 
 | 100 | 19.58 | 6.98 | 15.7 | 8.95 | 7.6214 | 14.656 | 8.2143 | 11.657 | 7.73 | 14.37 | 8.07 | 11.24 |  |  |  | 
 | 200 | 16.29 | 15.66 | 17.13 | 20.06 | 19.625 | 18.491 | 16.721 | 17.444 | 19.57 | 18.15 | 16.48 | 17.07 |  |  |  | 
 | 300 | 9.22 | 9.18 | 10.06 | 9.95 | 7.9106 | 9.9677 | 9.6936 | 9.2179 | 7.97 | 9.87 | 9.88 | 9.23 |  |  |  | 

## Slide 15: Appendix: CDF of RSRP gap in UMi-AV
Source 5

## Slide 16: Appendix: CDF of RSRP gap in UMa-AV
Source 5

## Slide 17: Appendix: Percentage of UEs with at least N strong interfering TPs in UMi-AV
N | TU@1.5m | AV@50m | AV@100m | AV@200m | AV@300m
1 | 39.9% | 78.2% | 83.1% | 83.4% | 82.7%
2 | 16.7% | 58.9% | 66.1% | 65.4% | 65.8%
3 | 7.5% | 39.7% | 51.3% | 51.5% | 48.4%
4 | 3.4% | 23.7% | 35.4% | 39.2% | 33.0%
5 | 1.5% | 12.4% | 21.8% | 27.3% | 20.8%
6 | 0.7% | 5.4% | 11.4% | 16.5% | 11.9%
7 | 0.3% | 2.0% | 5.5% | 8.7% | 6.7%
8 | 0.1% | 0.7% | 1.9% | 4.2% | 3.5%
9 | 0.0% | 0.2% | 0.6% | 2.0% | 1.9%
10 | 0.0% | 0.0% | 0.2% | 1.1% | 0.8%
11 | 0.0% | 0.0% | 0.0% | 0.6% | 0.4%
12 | 0.0% | 0.0% | 0.0% | 0.2% | 0.2%
13 | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
14 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
15 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
16 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Table 1 Percentage of UEs with at least N strong interfering TPs corresponding to all same-type UEs at same height (UMi-AV)
Source 5

## Slide 18: Appendix: Percentage of UEs with at least N strong interfering TPs in UMa-AV
N | TU@1.5m | AV@50m | AV@100m | AV@200m | AV@300m
1 | 31.2% | 83.3% | 82.1% | 96.8% | 99.1%
2 | 7.9% | 64.2% | 67.0% | 89.7% | 92.2%
3 | 1.4% | 45.8% | 53.8% | 80.3% | 82.1%
4 | 0.3% | 29.8% | 42.1% | 67.4% | 68.0%
5 | 0.04% | 17.8% | 31.4% | 52.8% | 55.0%
6 | 0.005% | 9.6% | 21.8% | 37.8% | 42.6%
7 | 0.0% | 4.8% | 14.1% | 25.2% | 30.1%
8 | 0.0% | 2.1% | 8.3% | 14.4% | 19.9%
9 | 0.0% | 0.8% | 4.2% | 6.6% | 12.8%
10 | 0.0% | 0.3% | 1.9% | 2.0% | 5.8%
11 | 0.0% | 0.1% | 0.7% | 0.7% | 0.7%
12 | 0.0% | 0.0% | 0.3% | 0.3% | 0.1%
13 | 0.0% | 0.0% | 0.1% | 0.1% | 0.0%
14 | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
15 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
16 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Table 1 Percentage of UEs with at least N strong interfering TPs corresponding to all same-type UEs at same height (UMa-AV)
Source 5