## Slide 1
3GPP TSG RAN WG1 #92 R1-1705610
Sanya, China, 16-20 April 2018
Agenda Item: 7.1.2.3.3
WF on DM-RS scrambling with fallback DCIs
Huawei, HiSilicon, vivo, China Telecom, NEC, CEWiT, China Unicom, AT&T, IITH, Deutsche Telekom, Tejas Networks, Softbank, Sony, Fujitsu, IITM, ASUSTeK, Lenovo, Motorola Mobility, CMCC, ZTE, Sanechips, Intel, OPPO

## Slide 2: Motivation
It is unclear which DMRS scrambling ID a UE should assume when the unicast PUSCH or PDSCH scheduled by fall-back DCIs (DCI format 0_0 or DCI format 1_0)
Relying on cell ID as the default scrambling ID for this case has some drawback:
  Multiple UEs scheduled with fallback DCI will suffer from intra-cell interference in case of multi-TRP or multi-beam operation

## Slide 3: Proposal
After RRC configuration, if a PUSCH/PDSCH of a UE is scheduled by DCI format 0_0 or DCI format 1_0, the UE would assume DMRS scrambling ID 0 is transmitted, i.e., =0.
  Note: For the RRC reconfiguration case, the latest DMRS scrambling ID 0 before reconfiguration is used.