## Slide 1
3GPP TSG RAN1 #93
Busan, Republic of Korea, 21st – 25th May 2018
Agenda Item: 6.2.8.2
R1-1807529
Proposal on UCI transmission for collision with UL SPS repetition
LG Electronics

## Slide 2
HARQ
SPS PUSCH
SPS PUSCH
SPS PUSCH
SPS PUSCH
Drop
Non-SPS PUSCH
Drop
Drop
Subframe#n
UL grant
Subframe#n-1
Change the previous agreement as follows:
In case of collision between non-SPS PUSCH and a SPS PUSCH (that is part of a SPS repetition window) of the same TTI length in the same subframe/slot/subslot on a given carrier, the UE shall transmit non-SPS PUSCH transmission and drop/stop the remaining SPS PUSCH transmissions of the UL SPS repetition window.
HARQ-ACK of the colliding SPS PUSCH is transmitted via non-SPS PUSCH.
CSI of SPS PUSCH, if any, is dropped.
UCI of the remaining SPS PUSCH within the repetition window is dropped.
HARQ-ACK of the remaining SPS PUSCH within the repetition window is transmitted via non-SPS PUSCH if present, otherwise the HARQ-ACK is transmitted via (S)PUCCH