## Slide 1: WF on RSS timing offset for efeMTC
Ericsson, Qualcomm, Sierra Wireless, Sony, Intel
3GPP TSG RAN WG1 Meeting #93 R1-1807569
Busan, Korea, May 21st -25th 2018
Agenda item 6.2.6.1

## Slide 2: Background
Agreements
The periodicity of the first subframe of RSS is configurable to 160, 320, 640 and 1280 ms.
  In addition, time offset is configurable
(SFN_RSS mod P_RSS) = O_RSS. The first subframe of RSS is subframe 0 of SFN_RSS.
  Frame resolution of O_RSS is 5 bits

## Slide 3: Proposals
  RSS timing offset has the following resolution:
  160 ms: 1 frame
  320 ms: 1 frame
  640 ms: 2 frames, starting at SFN = 0
  1280 ms: 4 frames, starting at SFN = 0