## Slide 1: Offline summary on Wednesday
NTT DOCOMO, INC.
3GPP TSG RAN WG1 Meeting 93
Busan, Korea, 21st – 25th May 2018
Agenda item: 7.1.3.1.2
R1-1807772

## Slide 2: Proposals
Modify the yellow part as following
For a given SS set or across SS sets, the UE is not expected to be configured with PDCCH monitoring occasion/periodicity causing partial time-domain overlapping for the same CORESET.
  Partial-overlapping in time-domain for the same CORESET means the case of that the separation between two monitoring occasions is smaller than the CORESET duration but greater than 0.

## Slide 3: Proposals
For UE BD capability reporting y = integer(4, …, 16), at least for self-scheduling,
For UE not supporting CA with different numerologies, the reported value equally applies to all numerologies
For UE supporting CA with different numerologies,
  When the UE is configured with CA with the same numerology, the reported value applies
  When the UE is configured with CA with different numerologies, the reported value applies to each set of DL-CCs with the same numerology, i.e.:
    The number of BDs for a given numerology i is (Mi * y) per slot of the numerology i
    The number of CCEs for a given numerology i is (Ni * y) per slot of the numerology i
    If a UE is configured with DL-CCs of X0, X1, X2, X3, where Xi denotes the number of DL-CCs with the numerology i, the total number of (BDs or CCEs) for the DL-CCs with the numerology i is given by Floor{Xi / (X0 + X1 + X2 + X3) * (Mi or Ni) * y} per slot of the numerology i
      Where Mi and Ni represent the number of BDs and CCEs per slot specified for non-CA case, respectively

## Slide 4: Proposals
PDCCH with CRC scrambled by C-RNTI and CS-RNTI are not monitored on Type3-CSS on SCell
When a UE is configured with cross-carrier scheduling and CS-RNTI, the UE monitors DCI format(s) 0_1 and/or 1_1 with CIF with CRC scrambled by C-RNTI and CS-RNTI
  For CS-RNTI, the CIF field is used to indicate cross-carrier activation of SPS/configured grant Type2
When a UE is configured with dynamic BWP switching and CS-RNTI, the UE monitors DCI format(s) 0_1 and/or 1_1 with bandwidth part indicator with CRC scrambled by C-RNTI and CS-RNTI
  For CS-RNTI, the bandwidth part indicator field is used to indicate BWP switching and activation of SPS/configured grant Type2 simultaneously

## Slide 5: Proposals
Clarify agreements at RAN1#92bis meeting as below:
Agreements:
NW and UE maintain the same understanding on SSB/CORESET#0/SS#0 in connected_mode at least for non-broadcast PDCCH and for broadcast PDCCH
  Solutions FFS: joint session between DL control and BM
For the broadcast PDCCH, it is up to UE which common search space to monitor based on which SSB in both connected, in-active, and idle modes
Unicast PDSCH can be scheduled by a DCI associated with the CORESET #0

## Slide 6: Proposals
Working assumption: Clarify Case 1 and Case 2 as following:
  Case 1: PDCCH monitoring of all SS sets that are monitored in a slot occurs at most at one span of up to 3 consecutive OFDM symbols periodicity of 14 or more symbols
    Case 1-1: PDCCH monitoring on up to three OFDM symbols at the beginning of a slot
    Case 1-2: PDCCH monitoring on any span of up to 3 consecutive OFDM symbols of a slot
      For a given UE, all search space configurations are within the same span of 3 consecutive OFDM symbols in the slot
  Case 2: PDCCH monitoring of all SS sets that are monitored in a slot occurs at more than one span of up to 3 consecutive OFDM symbolsperiodicity of less than 14 symbols
    Note: this includes the PDCCH monitoring of up to three OFDM symbols at the beginning of a slot

## Slide 7: Proposals
Clarify the RAN1#92bis working assumption as following:
  For a common search space configured with RMSI-PDCCH-Config, osi-searchSpace, paging-searchSpace, and/or ra-searchSpace, DCI format 0_0/1_0 with C-RNTI is monitored in non-DRX occasions and in the corresponding monitoring window with the configured PDCCH monitoring periodicity/offset/occasions whenafter C-RNTI is available.
  For a common search space configured with RMSI-PDCCH-Config, osi-searchSpace, paging-searchSpace, and ra-searchSpace, DCI format 0_0/1_0 with CS-RNTI is monitored in non-DRX occasions with the configured PDCCH monitoring periodicity/offset/occasions whenafter CS-RNTI is available.

## Slide 8: Proposals
Having joint session among MIMO and DL control to address questions from RAN2 in the LS:

## Slide 9
R1-1806550 Intel
  Confirm the WAs at RAN1#91 meeting
    Delete “if configured”
    PRACH is configured for each BWP
R1-1806666 ETRI
  Collision b/w Type0A-CSS and SSB is handled by the same way as collision b/w Type0-CSS and SSB
R1-1806289 CATT
  Remove CORESET restriction in PDCCH-ConfigCommon
R1-1806142 Nokia
  Recommend RAN2 to support a configuration of searchSpaceSIB1 by pdcch-ConfigSIB1 or SearchSpace by choice in PDCCH-ConfigCommon
R1-1806729 Samsung
  Adding periodicities {5ms, 10ms, 20ms, 40ms, 80ms, 160ms} and slot-level monitoring occasions for the RRC IE SearchSpace
R1-1807353 QCM
  Remove additional CORESET in the PDCCH-ConfigCommon
R1-1806055 vivo
  Type0/0A/1/2-CSS is configured by PDCCH-ConfigCommon for each DL BWP
R1-1806127 ZTE
  CORESET for Type0A/2-CSS is same as that for Type0-CSS only when these CSSs are in the same BWP
R1-1807160 ETRI
  Support NW-based and UE-based switching of CORESET#0 for unicast PDSCH

## Slide 10: Proposals
Having joint session between BWP and PDCCH on the following issues:
  Whether RAN1 can agree that each active DL BWP always contain SSB?