## Slide 1: Maintenance for NR-LTE co-existence
Qualcomm
R1-1809431
3GPP TSG RAN WG1 #94
Gothenburg, Sweden, August 20 - 24, 2018
Agenda item 7.1.4
Revision of R1-1807865

## Slide 2: Background
RAN1 has considered two UE types
  UE capable of dynamic power sharing, a.k.a. Type 1
  UE not capable of dynamic power sharing, a.k.a. Type 2
In the EN-DC power control procedure, RAN1 has considered that ‘NR’ in the Type 1 UE modem knows about ‘LTE’ but not the other way around
  This is because the different time-lines between LTE and NR
    This resulted in the decision of not changing LTE power by RAN1 power control definition for Type 1 UEs
    This resulted in the decision of not supporting sTTI in EN-DC

## Slide 3: Background
The 4ms LTE timeline has always been assumed for LTE
  E.g. no look-ahead in LTE CA or LTE DC
R1-143517, WF on “look-ahead” aspect in asynchronous dual connectivity, Ericsson, NTT DoCoMo, Softbank, Nokia Networks, Nokia Corporation, Alcatel-Lucent Shanghai Bell, Alcatel-Lucent
Agreements:
  At least for PUCCH and PUSCH, for asynchronous dual-connectivity,
    All remaining power is first made available to CG associate with earlier transmission
      No-Look-ahead (for the case that transmission timing difference is larger than around 33 micro sec) is specified as the UE behavior
  Definition of synchronous and asynchronous dual-connectivity is according to RAN4
    Timing relationship in any TA groups should be clarified in RAN4
  FFS: For asynchronous dual connectivity with the case that transmission timing difference is very small (e.g., around 33 micro sec)

## Slide 4: Background
The same assumption (no LTE look-ahead) has been made for EN-DC
R1-1715185, Way forward on power sharing for LTE-NR NSA operation, Ericsson, CATT, Samsung, Mediatek, Nokia, NSB
Agreements:
At least for LTE-NR NSA operation
  Maximum allowed power values for LTE (P_LTE) and NR (P_NR) are set separately
    i.e., when UE is configured for NR, P_LTE can be configured up to P_cmax and P_NR can be configured up to P_cmax.
    e.g. P_LTE + P_NR > P_cmax or P_LTE + P_NR = P_cmax
  Signaling details for P_LTE, P_NR are left to RAN2, RAN4.
  Note: ‘P_cmax’ is a limit that is similar to ‘The configured maximum UE output power’ that was specified for LTE.
  Note: The network will still have flexibility to prioritize or reserve certain NR transmission power depending on network implementation
  All UEs are mandated to handle P_LTE + P_NR = P_cmax while handling of P_LTE + P_NR > P_cmax depends on UE capability
  At least, when DL/UL LTE sTTI/reduced UE processing time based operation is not configured for the UE, if total transmit power exceeds P_cmax when there is simultaneous NR and LTE UL tx,
    For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation (note: it is not intended to have RAN4 test from RAN1 perspective)
      If there are two or more UL carriers, the power scaling or tx dropping can be performed for each of the UL carriers separately or jointly up to UE implementation
    For LTE, no change in power control procedure
  FFS the case when DL/UL LTE sTTI/reduced UE processing time based operation is configured for the UE
  The following is FFS
    The case when P_NR is configured such that P_NR < P_cmax, and UE can use power up to P_cmax in NR when it knows that there will be no UL transmission in LTE by semi-static configuration (e.g., measurement gap, DL/UL configuration)

## Slide 5: Background
RAN4 has defined MPR/A-MPR definitions [R1-1807805, “LS on RAN4 agreement on intraband EN-DC A-MPR”], which made different set of assumptions
  ‘LTE side knows about NR side’, even if NR UL grant arrives much later than LTE grant
  LTE PHR has a dependency on NR grant, even if NR UL grant arrives much later than LTE grant
The RAN4 decisions require substantial changes in the LTE processing time requirements, even though the NR Work Item was aimed to minimize impact resulting from NSA to LTE physical layer

## Slide 6: Background
Consider that LTE and NR use different slot formats, numerologies, the situations depicted below will occur for Type 1 UEs
The RAN4 decision results in LTE power changes within the LTE subframe, which is not supported in the LTE air-interface

## Slide 7: Background
FDD Example
TDD Example

## Slide 8: Background
Example
MPR/A-MPR change

## Slide 9: Proposal 1 (MPR/A-MPR, Option A)
Change in power dropping rule
  (1) the UE calculates LTE power (P_LTE_only) considering no NR Tx
  (2) the UE calculates NR power (P_NR_only) considering no LTE Tx
  (3) the UE calculates the LTE power (P_L) and NR power (P_N) according to the dynamic power sharing rule and RAN4 MPR/A-MPR definition
  (4) the UE performs the following
    If both P_LTE_only == P_L && P_NR_only == P_N
      UE transmits LTE and NR at powers P_L and P_N, respectively
    Else
      UE chooses a new P_N’ power within the bounds 0 <= P_N’ < P_N
      UE determines LTE power P_L’ based on P_N’
                If P_N’ == 0, P_L’ = P_LTE_only
                Elseif P_N’ == P_N, P_L’ = P_L
                Else P_L < P_L’ < P_LTE_only
      UE transmits LTE and NR at powers P_L’ and P_N’, respectively

## Slide 10: Proposal 1 (MPR/A-MPR, Option B)
Conditional power control operation based on timeline requirements being met
  If a Type 1 UE is configured with intra-band EN-DC, and the LTE UL transmission overlaps with an NR transmission, even partially, and
    if the NR transmission is grant based (e.g. PUSCH, A-CSI, A-SRS) and the grant triggering the NR UL transmission is meeting the LTE timeline
      i.e. the NR grant is no later than the first three symbols of the NR slot starting 4 ms before the start of the LTE subframe containing the LTE transmission in the case of LTE FDD or no later than the associated LTE DL control in the LTE TDD HARQ timeline in the case of LTE TDD
    And if the NR transmission carries HARQ-ACK and the latest NR PDSCH to which the HARQ-ACK corresponds and the NR DL control associated with that PDSCH both meet the LTE HARQ timeline
      i.e. NR PDSCH ends no later than 3 ms before the start of the LTE UL subframe in the case of LTE FDD or no later than the associated LTE PDSCH in the LTE TDD HARQ timeline in the case of LTE TDD, and similar conditions are met for the NR DL control granting the NR PDSCH
  Follow the existing RAN1 and RAN4 definitions
  Otherwise, follow the procedure describe in the previous slide (i.e. Option A)

## Slide 11: Example RAN1 specification changes for Option A
Possible text proposal to implement Proposal 4, Option A

## Slide 12: Proposal 2 (PHR)
Change in the LTE PHR requirement
  The UE is not expected to update LTE PHR report if the LTE reporting timeline is not met
    i.e. UE does not need to include in the PHR determination any information received later than 4ms prior to the PHR reference UL subframe in the case of LTE FDD, or later than the associated DL control in the TDD HARQ timeline in the case of LTE TDD

## Slide 13: Proposal 3 (Phase continuity)
The proposal in the previous slide already avoids phase continuity issues when LTE and NR use different PAs
There is still a phase continuity problem in the cases of intra-band EN-DC with common PA

## Slide 14: Proposal 3 (Phase continuity)
In order to solve the phase continuity issue, adopt the following for both Type 1 and Type 2 UEs
  When the LTE and NR Tx overlaps
    The transmission boundaries are aligned
      Same start and end times
    Frequency hop boundaries are aligned
      Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary
Possible text proposal to implement the above

## Slide 15: Proposal 4 (FR1 and FR2)
Since there is no joint FR1+FR2 power cap, the EN-DC power control procedures apply only to FR1
Clarify this in the specification

## Slide 16: Proposal 5 (TDM)
Clarify in the RAN1 EN-DC procedures that a UE indicating single Tx capability is not expected to be configured with simultaneous transmission in the MCG and SCG (both for TDM Case 1 and Case 2)