## Slide 1: WF on Extreme Long Range KPI Evaluation
Qualcomm Incorporated, [Nokia]
3GPP TSG RAN WG1 #85 R1-165485
Nanjing, China, May 23 - 28, 2016
Agenda item: 7.1.2

## Slide 2: Background
RAN plenary requirements (38.913) specified deployment scenarios for extreme rural and extreme long range services
Additional RAN1 agreement from RAN1#85 chairman notes:
  For the evaluation of Long Range (single cell SLS), consider a single cell radius target (e.g. 100km), and identify the data rate with which the edge users can be served; then observe how many users such a cell site can serve.

## Slide 3: Proposed Evaluation Assumptions
Attributes | Values or assumptions
Carrier Frequency | Around 700MHz
System Bandwidth | 40MHz (DL+UL)
Layout | Single layer: Isolated Macro cells
Cell range | 100 km range (Isolated cell) to be evaluated through system level simulations. Feasibility of Higher Range shall be evaluated through Link level evaluation (for example in some scenarios ranges up to 150-300km may be required).
Tx power | BS: FFS (should be >> 49 dBm) UE: 23 dBm
BS antennas | Up to 256 Tx/Rx
BS antenna pattern | Following the modelling of TR36.873
BS antenna height | FFS (should be >> 35 m)
BS antenna gain | FFS (should be >= 8 dBi)
BS receiver NF | FFS (should be <= 5 dB)
UE antennas | Up to 8 Tx/Rx
UE antenna height | Following the modelling of TR36.873
UE antenna gain | Following the modelling of TR36.873
UE receiver NF | 9 dB
User density and UE speed | User density: NOTE1 UE speed: Up to 160 km/h [50%], 3km/h [50%]
Traffic model | Average data throughput at busy hours/user: 30 kbps Target user experienced data rate: to be provided based on link budget analysis
Channel model | FFS
NOTE1: Evaluate how many users can be served per cell site when the range edge users are serviced with the target user experience data rate.

## Slide 4: Proposed Link Budget Evaluation
Recommended requirements in TR 38.913 on extreme long range:
  [Traffic density: [380-500kbps/km²]
  User Experienced Data Rate: up to [2]Mbps while stationary and [384kbps] while moving]
Aiming to have link budget analysis in RAN1#86:
  Channel model for extreme rural scenario
  Target data rate DL 2 Mbps (stationary) and 384 kbps (moving) with corresponding BS Tx power, BS antenna height, BS antenna gain, BS receiver NF
  Alternative DL data rate with corresponding BS Tx power, BS antenna height, BS antenna gain, BS receiver NF
  UL data rate with corresponding BS Tx power, BS antenna height, BS antenna gain, BS receiver NF
  Decision on remaining parameters in the SLS evaluation table