## Slide 1: WF on channel coding evaluation
Qualcomm
3GPP TSG RAN WG1 #85 R1-165492
Nanjing, China
23rd – 27th May 2016
Agenda item: 7.1.5
Document for decision

## Slide 2: Background
Individual contributions may not reflect best comparison for decision
  Limitations in construction availability, incomplete evaluation results, etc.
Results across companies should be more closely incorporated
  Allows proper identification for areas to improve NR channel coding
Chart: SNR to Achieve BLER=1% for 64-QAM R=8/9
| 100 | 400 | 1000 | 2000 | 4000 | 6000 | 8000
Polar (R1-164377) | 18.97 | 18.77 | 18.52 | 18.52 | 18.37
Turbo (R1-164186) | 21.8 | 19.75 | 19.75 | 18.9 | 18.85 | 18.85
LDPC (R1-164698) | 21.19 | 19.65 | 18.97 | 18.61 | 18.35 | 18.2 | 18.11
Chart: SNR to Achieve BLER=1% for QPSK R=1/5
| 100 | 400 | 1000 | 2000 | 4000 | 6000 | 8000
Polar (R1-164377) | -2.7294 | -3.2294 | -3.4794 | -3.6794 | -3.7794 | -3.8794 | -3.9294
Turbo (R1-164186) | -2 | -2.7 | -3 | -3.1 | -3.2 | -3.2
LDPC (R1-164698) | -2.2 | -3.3 | -3.7 | -3.9 | -4 | -4.1 | -4.1
Polar results unavailable for lower block length 64-QAM
(Rate 1/5 turbo code to be included)

## Slide 3: Proposal
Incorporation of raw data for summary analysis based on contributions provided at RAN1 #85
  Include assumptions and constructions, determine level of variance (after calibration) whenever constructions are shared
  Summary analysis is based on cross-comparison
Further study
  Take existing code designs and evaluate directly on fading channels
  Ensure code design enhancements are carefully evaluated across all operating regions
    Important when code technique allows efficient HW re-use across all operating rates