## Slide 1: WF on NB-IoT UL DMRS Hopping
Qualcomm,
R1-165630
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, May 23–27, 2016
Agenda item 6.1.6

## Slide 2: Background
In NB-IoT, different numbers, M, of DMRS base sequences are defined:
  M=30, for 12 tones
  M=14, for 6 tones
  M=12, for 3 tones
  M=16, for single tone
The cross-correlations between pairs of sequences can often be high.
UL DMRS hopping has yet to be defined.
  Without hopping, persistent interference may occur and lead to incorrect channel estimation even without noise.

## Slide 3: Proposal
To adopt the legacy LTE group hopping, as defined in Sec. 5.5.1.3, TS36.211, for NB-IoT UL DMRS:
  The group hopping pattern is revised from legacy LTE, based on the number of base sequences
    M=30, 14, 12, and 16 for, respectively ,12-tones, 6-tone, 3-tone and single-tone cases.
  The group-hopping pattern is reset every RU.