## Slide 1: WF on Implementation of cluster delay and angle spread
Ericsson, NTT DOCOMO, ZTE Corp, ZTE Microelectronics
R1-165772
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, May 23-27, 2016
Agenda Item: 7.2.3.3

## Slide 2: Background
In R1-165183, following Alternatives are described to implement cluster delay and angle spread.
  Alternative 1: Implementation for narrow BW based on sub-cluster information of 3GPP 3D channel model
  Alternative 2
    Alternative 2a: Method using generating step of cluster delays and angles in the 3GPP 3D channel model
    Alternative 2b: New method
      This method was agreed for the map-based hybrid model and is captured in the agreed TP in R1-165667

## Slide 3: Proposals
Following are proposals.
Proposal 1: Alternative 1 is adopt for low complexity simulations where narrow BW
  When no intra-cluster delay spread is specified the value 3.91 ns is used
    Note: This results in the legacy behavior with 5 and 10 ns sub-cluster delays
Proposal 2: Alternative 2b is adopt for large BW and/or large arrays
  Note: The agreed text in section R1-165667 relating to alternative 2b can be reused for the stochastic model