## Slide 1: WF on CSI-RS and Codebook Size for NR Ericsson, NTT DOCOMO, Huawei, LG Electronics, Nokia, ASB
3GPP TSG RAN1 #87 R1-1613362
Reno, USA, 14th – 18th November, 2016
Agenda Item: 7.1.3.3

## Slide 2: Background
From RAN1#86bis
  Agreements:
  Support NR CSI-RS pattern with at least the following properties:
    CSI-RS mapped in one or multiple [consecutive] symbols
    FFS: At least CSI-RS located at the earlier part of a slot in some cases
      FFS: before or after the DM-RS agreed to study in RAN1#85
    FFS: CSI-RS located at other part of a slot
    Working assumption: Configurable density of CSI-RS in frequency and/or time domain by UE-specific manner
    Working assumption: CSI-RS for NR should support up to 32 ports
      FFS: whether or not to have 32 ports codebook
  Support at least following configurations of NR CSI-RS
    UE-specific configuration to support
      Wideband CSI-RS, i.e. from UE perspective, the full bandwidth the UE is configured to operate with
      Partial-band CSI-RS, i.e. from UE perspective, part of the bandwidth the UE is configured to operate with
      FFS: Different patterns may be used for wideband and subband CSI-RSs

## Slide 3: Background
From RAN1#86bis
  Agreements:
    CSI-RS configuration for NR includes at least ‘number of antenna ports’
      Configuration can be explicit or impliit
    The number of CSI-RS antenna ports can be independently configured for periodic/semi-persistent CSI reporting and aperiodic CSI reporting
    Working assumption:
    The number of antenna ports supported for CSI-RS configuration includes at least the following values
      1,2,4,8,[12],16,[20],[24],[28],32
    RAN1 will update/remove above bracket parts in the next meeting
      Study e.g., performance, scenario, RS overhead, RS pattern considering the frame structure, reuse of hardware between NR and LTE

## Slide 4: Proposal
In NR, a UE can be configured with a CSI-RS resource configuration with X ports
  Supported values of X are up to at least 32
NR supports up to at least 32 port codebook
  FFS: Codebook design
Study the potential benefits of 64 ports