## Slide 1
Way Forward on handling of PDSCH/sPDSCH assignments for the same subframe and carrier
Ericsson, LG Electronics, Huawei, HiSilicon
R1-1613397
3GPP TSG RAN1 #87
Reno, Nevada (US), Nov 14 - 18, 2016
Agenda item 6.2.10.2.1

## Slide 2: Background
In RAN1#84 bis, the following agreements were made. However, the last bullet was mistakenly not captured in the TR. To our understanding, the last bullet can not be considered as a formal agreement for usage in the WI and has to be approved again in the WI.
For a UE to be dynamically scheduled with PDSCH and sPDSCH on a subframe granularity, the UE should search for DL assignments in both 1ms control channel and short TTI control channel
If a UE can be dynamically scheduled with PDSCH and sPDSCH, the UE behavior in case that valid assignments for both PDSCH and sPDSCH were detected in the same subframe needs to be defined.

## Slide 3: Proposal (1)
A UE can be dynamically (with a subframe to subframe granularity) scheduled with legacy TTI unicast PDSCH and/or short TTI unicast PDSCH
UE configured with sTTI shall monitor both DCI and sDCI in the same subframe for DL assignments
  FFS: Activation/deactivation of sTTI monitoring for UEs configured with sTTI, and further methods to reduce number of blind decodes and UE power consumption

## Slide 4: Proposal (2)
If valid DL assignments are detected based on C-RNTI/SPS C-RNTI in PDCCH/EPDCCH for PDSCH and PDCCH/sPDCCH for sPDSCH in the same subframe for a given carrier, the UE should decode the sPDSCH and may decode PDSCH
  UE shall provide HARQ-ACK feedback for both PDSCH and sPDSCH