## Slide 1: Way Forward on eMBMS enhancements
Ericsson, Intel, Qualcomm, EBU, IRT, BBC, DISH
R1-1613580
3GPP TSG RAN WG1 Meeting #87
Agenda item 6.2.4

## Slide 2: Proposal
Revised Working Assumption from RAN1#86bis
  For 100% MBSFN subframe allocation FeMBMS carrier transmits a periodic subframe, CAS Cell Acquisition Subframe
  CAS supports PSS, SSS, CRS, PBCH, PDCCH, PDSCH (SI)
  CAS is always transmitted in subframe #0 with a period of 40ms
  MIB is provided by PBCH in every CAS
  The MIB is transmitted in SFN mod 4 = 0 and can change only in SFN mod 16 = 0 and contains systemFrameNumber equal to the 6 most significant bits of the SFN
  SI can be provided by PDSCH in CAS
  A first SI that may also contain scheduling of further SI can be transmitted in SFN mod 8 = 0 and can change only in SFN mod 16 = 0
  This first SI may be a combination of SIBs, up to RAN2 agreements.
  MCCH change notification and SI modification notification are sent in PDCCH region of the CAS.
  From RAN1 perspective, it is feasible to transmit multiple SI messages in the same subframe by using different RNTIs. RAN2 may consider if this may be used.
  Inform RAN2 that SI modification notification can be conveyed to the UE with Direct Indication signalling.

## Slide 3: Proposal
  For a Rel-14 FeMBMS carrier operating with less than 100% MBFSN subframe allocation, the current DCI format 1-C used to indicate MCCH change, is extended to also indicate SI change.
  For PBCH in the CAS uses a different scrambling sequence initialization than for legacy PBCH.

## Slide 4: Proposal
  unicast control region
    cross-carrier scheduling is supported
      PHICH in PCell
    If a UE is configured with self-carrier scheduling, the UE shall assume that unicast control region (including CRS) is always present in all MBSFN subframes.
    For an FeMBMS carrier
      A UE shall not assume that unicast control region (including CRS) is always present in an MBSFN subframe not assumed to be used for PMCH.
      A UE can assume that unicast control region (including CRS) is always present in an MBSFN subframe assumed to be used for PMCH with 15kHz numerology.
      A UE can assume that unicast control region (including CRS) is never present in an MBSFN subframe assumed to be used for PMCH with 1.25kHz numerology.

## Slide 5: Proposal
  new CP subframe allocation
    subframes do not need to be allocated in a consecuetive pair