## Slide 1: WF on TPC accumulated mode for eLAA
Sharp, Huawei, HiSilicon, Intel, Kyocera, Nokia, Alcatel-Lucent Shanghai Bell, NTT DOCOMO, Qualcomm, Samsung, WILUS Inc.
3GPP TSG RAN WG1 Meeting #87
Reno, US 14th - 18th November 2016
Agenda item: 6.1.7
R1-1613752

## Slide 2: Background
It was agreed in RAN1#84bis Email discussion [84b-04]
  UL TPC per MSF
    UL TPC applies for all subframes non-cumulatively in both accumulated and absolute modes

## Slide 3: Background
TPC command in a UL grant applies to the 1st PUSCH scheduled by the UL grant
TPC command in subframe n applies to subframe n+4.

## Slide 4: Background
With Option 1, TPC command #1 and #2 apply to PUSCH1 and PUSCH2, respectively.
With Option 2, both TPC command #1 and #2 apply to both of PUSCH1 and PUSCH2.

## Slide 5: Proposal
Option 1 is applied to PUSCH TPC accumulated mode for eLAA.