## Slide 1: WF on UE-UE CLI measurement
Huawei, HiSilicon, ZTE, Vivo, CMCC, Samsung
3GPP TSG RAN WG1 Meeting #90 R1-1714799
Prague, Czech Republic, 21-25 August 2017
Agenda item: 6.1.5.1

## Slide 2: Background
Agreements:
For CLI management, support UE-to-UE interference measurement and reporting without the introduction of new RS(s)
Agreements:
For UE-to-UE interference, support CLI measurement metrics which include at least one of
  RSRP for the purpose of CLI
    FFS the definition (e.g., based on SRS, DM-RS, etc.) and the corresponding reporting
  RSSI for the purpose of CLI
    FFS the definition (e.g., resources for the measurement) and the corresponding reporting
For UE-to-UE interference, FFS additionally support CQI/CSI as the CLI measurement metrics and if so, its definition/reporting
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Proposal
Definitions of metrics for CLI:
  SRS-RSRP:
    Linear average of the power contributions of the SRS to be measured over the configured resource elements within the considered measurement frequency bandwidth in the time resources in the configured measurement occasions
  RSSI:
    The linear average of the total received power observed only in certain OFDM symbols of measurement time resource(s), in the measurement bandwidth, over the configured resource elements for measurement by the UE

## Slide 4: Proposal
For SRS-RSRP based UE-UE CLI measurement
  At least SRS can be used for UE-UE CLI measurement
  The specification should provide a mechanism for the network to configure a same SRS sequence for one or more UEs transmitting SRS
    Note: This intends to support cell-level, UE-group-level, and UE-level interference differentiation
  UE can be configured with SRS resource(s) (including time-frequency resource(s), sequence(s), cyclic shift(s), periodicity, etc) to measure UE-UE CLI interference.
    FFS details, e.g. configuration signaling, measurement triggering mechanism
    Every SRS resource has to be explicitly configured, i.e. there is no SRS ID acquisition by the UE required.
  Mechanism to limit the UE complexity for UE-UE CLI measurement is supported
    FFS details , [e.g. by limiting the number of root sequence of SRS for UE-UE CLI measurement that a UE needs to detect within a certain amount of time, longer periodicity.]
    FFS whether there is spec impact.
  FFS: The specification should provide a mechanism to avoid potential DL transmission interfering the SRS for UE-UE CLI measurement
    FFS exact details, [e.g. by rate matching the DL transmission around the SRS]
  FFS: Transmission timing advance of SRS for CLI measurement can be different from the transmission timing advance of its PUSCH, e.g D2D channel transmission timing
  The UE is not required to perform time tracking or time adjustment relative to DL operation in order to perform RSRP measurement.

## Slide 5: Proposal
For RSSI based UE-UE CLI measurement
  UE can be configured with a set of resource elements to measure UE-UE CLI interference.
    FFS details, e.g. the set of resource elements can be SRS resource, configuration signaling, measurement triggering mechanism
  FFS whether additional mechanism for SRS transmission is needed for RSSI based UE-UE CLI measurement
  FFS: The specification should provide a mechanism to avoid potential DL transmission in the RSSI measurement resource elements for UE-UE CLI measurement
    FFS exact details, e.g. by rate matching the DL transmission around the resource elements for RSSI UE-UE CLI measurement