## Slide 1: WF on PDSCH and PUSCH rate matching behavior
LG Electronics, Intel, Samsung, Ericsson, NTT DOCOMO
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August 2017
Agenda item: 6.1.2.1.7
R1-1715033

## Slide 2: Background
In RAN1 Ad-hoc #2 meeting, following agreements are captured in the Chairman’s note as
  A UE is configured with resources for PDSCH rate matching
    FFS details
  A UE is configured with resources for PUSCH rate matching
    FFS details

## Slide 3: Proposal
By default, PDSCH is at least rate matched around REs indicated for the following signals.
  NZP CSI-RS resource(s) for channel measurement
  DMRS for PDSCH for the UE.
  DL PTRS
  TRS
  FFS: NZP CSI-RS for interference measurement
  Note: PDSCH rate matching for DL control channel, SS block, reserved resource are out of MIMO scope.
By default, PUSCH is at least rate matched around REs indicated for the following signals.
  DMRS for PUSCH for the UE.
  SRS
  Note: PUSCH rate matching for UL control channel, reserved resource are out of MIMO scope.