## Slide 1: WF on carrier configuration for duplicated SL LCHs
Huawei, HiSilicon
R2-1808918

## Slide 2: Issue to address
For Mode 3, whether it is
  Opt1: two orthogonal carrier Sets, or
  Opt2: two different carriers
  that shall be configured per Destination for all PPPR(s) configured for SL packet duplication.

## Slide 3: Demo of Opt1 and Opt2
PPPR=1, DST=1
{F1, F2, F3}
{F4, F5}
PPPR=1, DST=1
{F1}
{F5}
OPT1:
OPT2:
Duplicated SL LCH1
Duplicated SL LCH2
Duplicated SL LCH2
Duplicated SL LCH1

## Slide 4: How the two options work?
For Opt1:
  The data of a duplicated SL LCH is transmitted by the SL grant scheduled on any carrier included in the associated carrier set (e.g. in the last page, data of duplicated LCH1 can be sent as long as there’s SL grant on either F1, F2 or F3, as decoded from PDCCH);
  Data of a duplicated SL LCH can rely on multi-carrier transmission as per eNB scheduling;
  How many carriers are included in a carrier set is up to eNB implementation, similar to NR PDCP duplication (i.e. allowedServingCells).
  For Opt2:
  The data of a duplicated SL LCH can only be transmitted on the SL grant scheduled on one associated carrier (e.g. in the last page, data of duplicated LCH1 can be transmitted only if there is SL grant on F1, as decoded from PDCCH);
  Data of any duplicated SL LCH can only be transmitted on a single carrier, no matter how eNB schedules.

## Slide 5: Comparison of Opt1 and Opt2
Observation 1: In Opt 1, data of a duplicated SL LCH can be sent with the SL grant assigned on any carrier included in the associated carrier set; whereas in Opt 2, data of a duplicated SL LCH can only be transmitted on the single carrier associated with it.
Observation 1a: Based on Observation 1, the data of a duplicated LCH can enjoy multi-carrier transmission in Opt1 (which may be good for Tx rate), whereas data of a duplicated LCH can only rely on single-carrier transmission in Opt2 (which may limit Tx rate).
  Observation 2: For Opt 1, how many carriers included in each carrier set in Opt 1 is up to eNB implementation. If necessary, the eNB can configure a single carrier in the carrier set associated with each duplicated LCH, so that Opt1 can already cover Opt2.
  Observation 3: From NW perspective, Opt1 has more flexibility than Opt 2.
  Proposal 1: For Mode 3, two orthogonal carrier sets are configured per Destination reported in the SidelinkUEInformation (it is common for all PPPRs ,which meets PPPR threshold, configured for sidelink packet duplication).
  Proposal 2: For Mode 3, two duplicated LCHs corresponding to the same PDCP entity are associated respectively with the two orthogonal carrier sets configured for the Destination of the duplicated LCHs (which LCH is associated to which carrier set is up to UE implementation).