## Slide 1: SN gap analysis

## Slide 2: SN gap analysis
Case 1: SDUs are discarded while stored in PDCP buffer
  Most viable solution for Case 1 is SN re-association, i.e. SDUs 9~12 are re-associated to SN 5~8.
  Even if the SDUs 9~12 are transmitted without SN re-association, the t-Reordering in the receiver would ensure the PDB.
  If discard notification is introduced, it could remove the reordering delay of one t-Reordering time. However, due to the transmission of discard notification, the transmission of SDUs 9~12 are delayed.
1
2
3
4
5
6
7
8
9
10
11
12
Transmitted SDU
Discarded SDU
Stored SDU
PDCP Tx buffer
Discard notification
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: SN gap analysis
Case 2: SDUs are discarded while stored in RLC buffer
  Depending on implementation, it may be difficult to re-associate SN for SDUs stored in RLC buffer.
  However, even if the SDUs 9~12 are transmitted without SN re-association, the t-Reordering in the receiver would ensure the PDB, same as in case 1.
  If discard notification is introduced, it is transmitted only after the SDUs 9~12 are transmitted. (There is no prioritization of PDCP Control PDU in RLC transmission). Then, the benefit of discard notification is much less than case 1, i.e. it reduces only a portion of one t-Reordering.
1
2
3
4
5
6
7
8
9
10
11
12
Transmitted SDU
Discarded SDU
Stored SDU
RLC Tx buffer
Discard notification
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: SN gap analysis
Case 3: SDUs are discarded discontinuously while stored in RLC buffer
  If pdu-SetDiscard is configured and if PDU sets are interleaved, SDUs stored in RLC buffer may be discarded discontinuously.
  If the SDUs 6, 8, 10, 12 are transmitted without SN re-association, the t-Reordering starts when the SDU 6 is received. The SDUs 8, 10, 12 are received while the t-Reordering is running. When the t-Reordering expires, another t-Reordering starts for SDU 12. Thus, the delivery of SDUs 8, 10, 12 are delayed until two t-Reordering expires.
  If discard notification is introduced, it is transmitted only after the SDU 12 is transmitted. Then, the benefit of discard notification is one t-Reordering + a portion of one t-Reordering.
1
2
3
4
5
6
7
8
9
10
11
12
Transmitted SDU
Discarded SDU
Stored SDU
RLC Tx buffer
Discard notification
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Observations
Current PDCP operation does not cause any critical problem.
Discard notification may be beneficial in following conditions:
  pdu-SetDiscard is configured
  PDU sets arrive at PDCP buffer with interleaving
  Lots of PDCP SDUs are pre-processed and stored in RLC Tx buffer
  RLC SDUs are not transmitted until the discard timer expires
In the above condition, the benefit of discard notification is reducing the reordering delay as one t-Reordering + a portion of one t-Reordering
Even if discard notification is introduced, the legacy behavior can still be applied; (Thus, the transmission of discard notification shall not be mandated even if it is configured.)
  SN re-association
  Relying on t-Reordering