## Slide 1: Fast/Parallel RRC Setup for MH relay
Offline-409
Apple
R2-2503078

## Slide 2: Offline-409
* [AT129bis][409][Relay] Fast/parallel RRC forwarding for approach 1 (Apple)
Scope: Discuss the forwarding procedure proposed in R2-2502189:
- Understand the expected spec impact and details of the proposal
- See if there is consensus to include this proposal in approach 1
Intended outcome: Report to Tuesday evening relay session in R2-2503078
Schedule: Tuesday 2025-04-08 0830-0930 CST in Brk2
Deadline: Report available by Tuesday 2025-04-08 1600 CST

## Slide 3: Motivation for Latency reduction
In baseline approach, the requirement for UEs entering RRC_CONNECTED sequentially causes significant delay, which is not scalable as the number of hops increases.
Latency reduction can be achieved by enabling parallel RRC connection setups of Remote UE and Intermediate Relay UE(s).
This is for Approach 1, assuming all relay UEs will still enter CONNECTED.
(Brief)Discussion on Motivation:
[LG,Huawei]: really critical or not? Latency is bad only when all relay UEs are not in CONNECTED. [Kyocera]: model B discovery does not require relay UE to connected.[HW]: RRC_State can be added in discovery message so remote UE only choose connected relay.[SS]Depends on frequency relay/traffic and relay RRC state.[ATT, IDT]:For mission-critical application, latency is an issue cover multiple hops. Keep UEs in RRC_CONNECTD cost NW resources. [NEC]:backward-compatibility issue for discovery-based solution. [IDT] R18 UEs are not supposed to understand R19 discovery message.[HW]:Consider always keep UEs in CONNECTED for Mission-critical cases.[OPPO]: Agree with the gains can be vary depends on scope and fine to move to technical discussion.

## Slide 4: How the Solution works in high-level
SRB0 message (e.g., RRCSetupReq/RRCSetup) forwarded by intermediate relay UEs not in RRC_CONNECTED [mainly TS 38.351 spec impact]
  Remote UE still use legacy mechanism to reach first intermediate relay
  Relay UE remembers which PC5 link received the first SRB0 message in UL and use it for DL egress link determination [ZTE: except the 1st relay as it knows the L2 ID via PC5]
  Discuss: Operation on Uu Relay RLC channel (last hop) kept unchanged? or keep SUI unchanged and change Uu SRAP operation
  Discuss: FFS a new SL-RLC is introduced (e.g., SL-RLC-X) or reuse SL-RLC0
Remote
1st relay
2nd relay
Last relay
gNB
RRCSetupReq
RRCSetupReq
RRCSetupReq
RRCSetupReq
RRCSetup
RRCSetup
RRCSetup
RRCSetup
SL-RLC0
SL-RLC0
SL-RLC0
Uu Relay RLC channel

## Slide 5: Discussion: How to Differentiate Remote UE
Option 1 (R2-2502189): SRAP header adding a L2 ID field to indicate remote UE in a new header format [mainly TS 38.351 spec impact]
Option 2 (R2-2502778): gNB allocated Local ID(s) to intermediate relay UE in RRCRelease when UE enter INACTIVE; relay UE then assign this local ID to represent remote UE when create SRAP header [mainly TS 38.331 spec impact]
[QC]Option 3: Remote UE assign local ID by itself in SRAP header in first-hop over SL-RLC0
  [OPPO] collision issue, other impact are similar to Option 1

## Slide 6: Further discussion on scope
Which RRC messages (of remote UE) can be fast forwarded?
  Option 1: Only SRB0
  Option 2: both SRB0 and SRB1
Which RRC state of intermediate relay UE to support?
  Option 1: IDLE/INACTIVE/OOC
  Option 2: INACTIVE

## Slide 7: Way-forward
Proposal: Consider parallel forwarding of RRC messages with the design constraints and scope limits as follows:
  - only for Uu SRB0 messages
  - keep 1st hop (remote-1st relay) operation on SL-RLC0 unchanged (same as legacy)
  Avoid RAN3 impact if possible
  At least for UL. FFS for DL
  FFS whether/how gNB understand path information
  FFS optional/mandatory of this feature for approach 1
  Checking TP (331/351,etc.) in RAN2#130 to decide whether to support this scheme based on 1)spec impact; 2) whether main technical issue unsolved.
Other solutions for latency reduction are still based on company contributions.