## Slide 1
[AT130][030][AIoT] RA (InterDigital)
Intended outcome: Discuss CB on collion handling and index/bitmap information in msg2 and discuss whether MSG2 transmission and any retransmission of MSG2 happens before the subsequent paging and/or trigger message from the reader. If time allows 2-6 issue
Deadline: Friday
Issue 1: When a device transmits MSG1, when should it expect to receive MSG2 from the reader?
Issue 2: Are there any technical issues with the use of index/bitmap in MSG2 to handle collision?
Issue 3 (if time): Whether to include the number of multiplexed RN16 in MSG2.

## Slide 2
Issue 1: When a device transmits MSG1, when should it expect to receive MSG2 from the reader.
From online discussion, timer-based approach is excluded:
=> Exclude option 1 and discuss offline before subsequent paging or subsequent trigger
Option A: Before next (subsequent) paging message
Option B: Before the next R2D Trigger Message
Option C (from offline discussion): Before a fixed number (K > 1; e.g. 2 or 4) of R2D trigger messages (see annex figure for motivation)

## Slide 3
Option A
  Device assumes MSG1 success when receiving RN16 before next paging, otherwise failure (failure is determined at subsequent paging message)
    MSG2 to support large number of RN16 (2^Q*X*Y (in the worst case))
    Increase RN16 collisions => reception of same RN16 in 2 of 2^Q*X*Y resources
    Latency for device in success case
Option B
  Device assumes MSG1 success when receiving RN16 before next R2D message (R2D trigger or paging, whichever is first)
    MSG2 to support at most (X*Y) RN16s
    Less RN16 collisions => reception of same RN16 in 2 of X*Y resources
    Less latency for device in success case
Option C
  Device assumes MSG1 success when receiving RN16 before the next K R2D trigger messages (or subsequent paging – whichever comes first)
    MSG2 to represent at most (X*Y)*K RN16s
    RN16 collisions over (X*Y)*K
    Latency for success case at most K R2D trigger messages

## Slide 4
Comments
{Apple} – Device can determine K from the maximum MSG2 size
{Fujitsu} – Can consider option B, but also command message
{QC} – Option B is simpler from device implementation. Not ok with Fujitsu proposal – HW has same understanding: command could be for someone else.
{HW} – Option C and Fujitsu is along same lines. Difference is how we define the short window. A may be too flexible.
{LG} – We can exclude option A. B is preferred to avoid checking how many messages
{E//} – Option B is simple and initial assumption. Preferrable given time.
{Lenovo} – Agrees to exclude option A. Option C allows some flexibility from the reader side – preferrable
{OPPO} – Option C is a superset of option B (i.e., K=1). Is K predefined or configurable? Prefer fixed {HW} – Either is possible. If configurable, we would need to send it in the paging message.
{Xiaomi} – Option A is not preferred. Option C – if we support, it should be fixed if we support. Otherwise B preferred. IDC agrees.
{Ofinno} – Exclude A. ZTE agree with.
{MDK} – Prefers option B, to avoid complexity. QC has same view. SAM agrees and thinks fixed does not give flexibility. HW clarifies it is for time limitation at the reader.
{CATT} – Support option C with fixed value.
{Apple} – prefer option C for flexibility. MSG2 can be retransmitted later (after an R2D trigger). Not concerned with complexity of option C.
{Vivo} – prefers option B for complexity at device.
{HONOR} – prefers B. Similar to MDK. Also need to consider missing trigger.
=> Exclude option A. Option B and Option C can be further discussed. For option C, further discuss in terms of complexity at the device vs reader flexibility.

## Slide 5
Issue 2: Are there any technical issues with the use of index/bitmap in MSG2 to handle collision?
MSG2 cannot resolve the collision by sending RN16 alone
=> MSG1 if FDM but MSG2 is not FDM
Indicating a time/frequency resource along with RN16 in MSG2
=> Option 1, T/F index with each RN16
        A: T-F index [X=2, Y=4 => 3-bit T-F index]
        B: F index only [X=2, Y=6 => 2-bit F index]
=> Option 2, bitmap of all time/frequency resources [X=4, Y=2 => 8- bit bitmap]

## Slide 6
FW – For option 1, only send TF for RN16 that have collision. If we consider option C, we would need slot index.
Xiaomi – T/F index to replace RN16, we would always need to include AS ID all the time. Option 1 is preferred. Lenovo agrees and agrees with FW. E// agrees – we can further check if we include only for colliding or not.
HW – Should still include RN16.
Vivo – Agree with HW. Can be bitmap.
Apple – Ok with feasibility. Related to option B or C.
QC – Agree with Apple. We have agreed with RN16. Whether needed for contention resolution – we would have increased the RN16 value. Option 2 has more bits. ZTE agrees with QC. Frequency is feasible, time may not be needed (depends on R2D triggers missed and analysis on whether needed).
DCM – Should not change RN16 agreement. Agrees with DCM – if we indicate T/F, device needs to remember.
HONOR – Thinks this is needed, and prefers bitmap.
E// - For time information, it is needed along with frequency. Either option is feasible.
Xiaomi – based on chair guidance, we should collect feasibility and not probability. Agrees with ZTE that time index has some issues. Does not see device complexity of remembering the frequency of transmission.
HW – Frequency Index is considered feasible. We should exclude time. MDK agrees. MDK also agrees with FW that we can indicate this only for the collision case.
=> Including Frequency index with RN16 is feasible for option B and C. Discuss further online whether to introduce the index.

## Slide 7
Issue 3: Whether to include the number of multiplexed RN16 in MSG2.
R2-2503420 Discussion on the Random Access for A-IoT CATT discussion Rel-19 Ambient_IoT_Solutions
Proposal 6: (2-6) The number of multiplexed RN16 in A-IoT Msg2 is explicitly indicated to the device. A bitmap is introduced with the same length as the number of multiplexed RN16 to indicate the allocated AS ID associated with the corresponding RN16.
R2-2504159 Discussion on UL multiple access Ericsson discussion Rel-19 Ambient_IoT_Solutions
Proposal 7 Msg2 need not contain an indication of the number of random IDs.
[Discussion]
- No time for discussion

## Slide 8
Conclusion of Offline for RA:
A device expecting MSG2 assumes failure if its MSG2 is not received before a boundary, where the boundary can be further downselected between option B and C below. A device receiving MSG2 within this boundary transmits MSG3. The device does not process MSG2 (re)transmission received after the boundary.
  Option B – the boundary is the reception of either the next R2D trigger message or the subsequent paging message
  Option C – the boundary is the reception of either the kth R2D trigger messages or the subsequent paging message (K is FFS)
  Option A (the boundary being the subsequent paging only) is excluded.
  For option C, further discuss in terms of complexity at the device vs reader flexibility.
Including frequency index along with RN16 in MSG2 to reduce collisions of MSG1 between different UEs is feasible. Discuss further whether to include it.

## Slide 9
Conclusion on discussion of NACK reception:
After MSG3 transmission, upon receiving NACK with its AS ID before subsequent paging or command addressed to this device from the reader, device determines it will perform re-access. FFS how to specify.

## Slide 10
Conclusion on RN16/AS ID maintainance:
FFS: A device is not expected to maintain both AS ID and RN16.

## Slide 11
Appendix: Option C (K=3)