## Slide 1: Discussion on SA2 LS on non-OTA data set transfer
RAN2#131-bis
R2-2507707

## Slide 2: Background
In R19, RAN1 were deciding between using a reference model (“Direction C”), and transferring data sets/model parameters (“Direction A”)
For “Direction A”, RAN1 asked RAN2 to comment on OTA and non-OTA options for this transfer
RAN2 found OTA option non-feasible
For non-OTA, RAN2 produced its own classification, made certain assumptions on data transfer through the core, and asked SA2 and SA5 to confirm these (or otherwise)
RAN2 sent an LS to SA2 to this effect (R2-2503169)

## Slide 3: The 3 options (RAN2 classification)
Option | Impacted WG | Specification impact/Implementation impact
OAM -> UE-side training entity (a server inside MNO or an OTT server), where OAM is NW-side dataset/model parameter collection entity – Option I | SA5, SA3 | Up to SA5 (any intermediate node between OAM and UE-side OTT server is up to SA5; CN involvement if needed is up to SA2/SA5 discussion)
CN -> UE-side training entity (a server inside MNO or an OTT server), where CN is NW-side dataset/model parameter collection entity – Option II | SA2, SA3 | Up to SA2 (any intermediate node between CN and UE-side OTT server is up to SA2)
gNB -> OAM/CN -> UE-side training entity (a server inside MNO or an OTT server), where gNB is NW-side dataset/model parameter collection entity – Option III | RAN3, SA2, SA5, SA3 | Up to RAN3, SA2, SA5 (any intermediate node between gNB/OAM, OAM/UE-side OTT server, CN/UE-side OTT server is up to RAN3/SA2/SA5)

## Slide 4: Reply from SA2 received in R2-2506751
Option III (CN variant) not supported in R19 SA2 specs according to above reply
As R19 is now behind us anyway, the key impact of this appears to be that – should we want Option III supported in R20, it would need to be added into R20 SA2 study

## Slide 5: Only one question raised in the reply-LS...
What RAN2 meant by different options is that NW-side collection entity is different
  For Option III, NW-side collection entity a CN node, whereas for Option II it’s the gNB
Q: SA2 are unsure what we meant by Option III/Option II, but they are sure R19 specs do not support Option III? Does their reply in previous slide therefore refer to CN UE side training entity part of the path?
Q: depending on how the transfer of this data then proceeds from CN to UE-side training entity, and gNB to UE-side training entity, these two options may or may not have the same impact on specs?
  It could be that CN handling of data in those two options is different?
  Should SA2 answer this instead of RAN2?

## Slide 6: ... And one indirect request made
Q: So long as RAN2 clarifies Option I/II/III in our reply to SA2, it appears any further information should come from RAN1?

## Slide 7: Proposed way forward
P1. Reply is sent to SA2 clarifying details of options (based on existing RAN2 agreements), and indicating that SA2 may make the final judgement on any difference between the three options.
P2. Advise SA2 that RAN1 (in cc) will provide input as and when needed on any further information pertaining to data set/model parameter transfer.

## Slide 8: Discussion
MTK: also unclear on the difference between options, is it just gNB involvement; is it just a matter of co-ordination between two different servers
Xiaomi: key difference is entity generating the data set but this was unclear in R19, which is why we kept the different options; from transport point of view, they agree with MTK
Nokia: do we really need to consider an SA2 solution, when OAM solution is available
Xiaomi: plan might be for RAN2 to down-select; SA2 already have a TU allocation for this so not urgent to send a reply LS
Vivo: December check point for RAN, we need input from SA2
Huawei: option 2 vs option 3 is about data content; option 2 is raw data

## Slide 9: Discussion (cont’d)
MTK: P1 ok with MTK; they are unsure if we need a standardised solution. P2 – MTK not ok with it; they would be ok with the following revision:
P2’. Advise SA2 that RAN1 (in cc) will provide input as and when needed on any further information pertaining to content of data set/model parameter.

## Slide 10: Revised way forward
P1. Reply is sent to SA2 clarifying details of options (based on existing RAN2 agreements), and indicating that SA2 may make the final judgement on any difference between the three options.
P2’. Advise SA2 that RAN1 (in cc) will provide input as and when needed on any further information pertaining to content of data set/model parameter.