## Slide 1: Way Forward for Fast RLF
Huawei, Hisilicon, Vodafone, MediaTek

## Slide 2: Fast RLF Trigger conditions
Proposal 1: Use Fast RLF as today:
  Start measurement for neighbour cell based on RSRP criteria,
  Neighbour cell better offset than serving cell: start T312, monitor recovery check
  T312 expires: move to the selected cell
  Need to create measurement gap
  Benefit: higher probability to find a better cell
    Proposal 2: New type of Fast RLF
  Detect PHY failure: start T310, start measurements of neighbour cells
  Neighbour cell better offset than serving cell: move to the selected cell
  T310 expires: normal RLF mechanism
  Benefit: do not need measurement gaps