## Slide 1: Way forward on RIM discussion
CMCC
3GPP TSG-RAN WG3 Meeting #104
Reno, Nevada, USA, May 13th – 17th, 2019
Agenda item: 16.3
R3-193228

## Slide 2: Key issues
Content of RIM message on NG and F1
Details of Stage 2 and Stage 3 CR
OAM impact

## Slide 3: Key issue #1
At last meeting, we clarify on the following assumption in summary of offline discussion (R3-192092)
  Assumptions:
  Each victim or aggressor gNB will be assigned a set ID, all the cells managed by gNB-DUs within the same gNB-CU will utilize the same Set ID.
RAN1 never discussed per-cell set ID, the agreement in R1-1903589 are made on per-gNB basis, i.e., at most two set IDs can be configured for a gNB, one for RS-1 and one for RS-2
To confirm each victim gNB can only has one Set ID configured or not
Parameter | Explanation | Value range
Value of set ID | Set ID for RS-1 Set ID for RS-2 (if configured) | At most two set IDs can be configured for a gNB. The bit length of the set ID is maximum 22bit.

## Slide 4: Key issue #1-Continue
A gNB may be assigned several set IDs and RIM-RS configurations simultaneously (TR 38.866)
  A gNB participating in an RI scenario may be a victim, an aggressor or both. The gNBs involved in an RI scenario can be grouped into sets. Each set is assigned a set ID, and is configured with a RIM Reference Signal (RIM-RS) and the radio resources to send and receive the RIM-RS. The grouping of gNBs into sets, the set ID, the RIM-RS configuration and the associated RIM-RS radio resources for sending and/or receiving the RIM-RS are performed by the OAM system, and these resources may be assigned in static or a non-static manner. A gNB may be assigned several set IDs and RIM-RS configurations simultaneously. Every gNB may have pre-configured set ID(s).
The gNB-CU may serve more than 16000 cells which belong to many gNB-DU. These gNB-DUs may belong to different RIM SETs. (TS 38.423：Maximum no. cells that can be served by a NG-RAN node. Value is 16384.)
To confirm each victim gNB can only has one Set ID configured or not
Conclusion 1: Each gNB can be configured with multiple set IDs

## Slide 5: Key issue #1
Common understanding the following information should be included
  Source gNB ID, source TAI
  Target gNB ID, target TAI
  Target set ID
  RIM –RS detection or RIM-RS disappearance
Views on other parameters from papers
Content of RIM message for NG interface
Proposal 1: RIM-RS detected and disappearance, Source gNB ID/TAI, target gNB ID/TAI and target set ID should be included in RIM backhaul message, other information are for FFS
Parameter | Needed | Not needed
Source set ID | Nokia, HW | Samsung, CMCC
Target set ID | ZTE (depending on conclusion of the set ID configuration) | Samsung, CMCC, HW, Nokia
Aggressor Cell ID | ZTE (optional), E/// (mandatory in RIM message) | Samsung, CMCC, HW, Nokia

## Slide 6: Key issue #1
DU to CU
  Common understanding the following information should be included
    RIM –RS detection or RIM-RS disappearance
    Target set ID
Content of RIM message for F1 interface
Parameter | Needed | Not needed
Source set ID | E///, HW | CMCC, Samsung, ZTE, Qualcomm
gNB-ID lists | Samsung (Optional) | CMCC, HW, ZTE, Qualcomm, E///
Cell ID | ZTE (optional), E/// | CMCC, Samsung, Qualcomm, HW
    Proposal 2: RIM–RS detection or RIM-RS disappearance information and target set ID should be included in RIM backhaul message from DU to CU, other information are FFS

## Slide 7: Key issue #1
CU to DU
  Common understanding the following information should be included
    RIM –RS detection or RIM-RS disappearance
Content of RIM message for F1 interface
Parameter | Needed | Not needed
Source gNB ID | CMCC, ZTE | Samsung, HW, Qualcomm, E///
Source set ID | Qualcomm, E///, HW | Samsung, CMCC
Target set ID | ZTE, E/// | Samsung, HW, CMCC
Cell ID | ZTE (Optional), E/// | Samsung, HW, CMCC
    Proposal 3: RIM–RS detection or RIM-RS disappearance information should be included in RIM backhaul message from CU to DU, other information are FFS

## Slide 8: Key issue #2
Stage 2 CR
    ZTE, HW, E///, Samsung have provided stage 2 CR,
    Not see much difference, it can be merged during the meeting
Stage 3 for NG
    NG-AP
      Alterative 1: define a new RIM transfer IE in RAN configuration transfer message. (HW, ZTE, Samsung, CMCC)
      Alterative 2: define RIM interference report IE inside existing SON information IE (Nokia )
      Alternative 3: define a new procedure (E///)
    F1-AP:
      Alterative 1: define new F1-AP messages (HW, ZTE, Samsung, CMCC, E///)
      Alterative 2: extend existing CU/DU configuration update messages (Samsung, Qualcomm)
Details of Stage 2 and Stage 3 CR

## Slide 9: Way forward
  Conclusion 1: Set ID can be configured on per-cell basis, i.e., each aggressor/victim gNB can be configured with multiple set IDs, but each aggressor/victim cell can only be configured with one set ID.
  Proposal 1: Agree to include the following information in RIM message, other information are FFS and to be decided online.
    NG
    Source gNB ID, source TAI
    Target gNB ID, target TAI
    Target set ID
    RIM –RS detection or RIM-RS disappearance
    F1 (DU to CU)
    RIM –RS detection or RIM-RS disappearance
    Target set ID
    F1 (CU to DU)
    RIM –RS detection or RIM-RS disappearance
Proposal 2: To decide on using new procedure or reusing existing procedure for NG and F1 signalling
  Proposal 3: CBs assigned to converge on the stage 2 and stage 3 CRs as well as the LS to RAN1/SA5, if needed