## Slide 1: Way Forward on Rel-17 NR MBS WI
Huawei, xxx
3GPP TSG-RAN WG3 #115-e R3-22xxxx
Online, 21st February - 3rd March 2022

## Slide 2: MBS2: Session Management
For BC:
  One procedure to include multiple Area Sessions for location dependent service
  Support RAN triggered BC Session Release procedure
For MC:
  Include Area Information(s) in Distribution Setup Response
  No QoS information and Area Information in Activation Request
  Stop discussion on SA2 Note 4

## Slide 3: MBS3: E1 F1 bearer management
In case RAN2 agree to introduce common MC CellGroupConfig
  Support PTP retransmission and PTP only F1-U bearers
  MC Session control via common procedures
In case RAN2 do not agree to introduce common MC CellGroupConfig
  Reuse existing F1/E1AP procedures to manage the multicast MRB related context/bearers.
  Introduce non-UE associated F1/E1AP procedures to setup and release the shared F1-U tunnel.
Note that in RAN2Offline043, there are 5 Yes, and 15 NO

## Slide 4: MBS5: HO between supporting nodes
Provide MBS information from Source to Target outside of PDU Session level IE, include associated QFI inside of PDU Session level IE.
Provide the MBS Progress (PDCP COUNT, QFI SN) from Source to Target, in Handover Preparation and Status Transfer.
Support Data Forwarding between supporting nodes.
  Provide the MBS Progress from Target to Source to stop data forwarding.
Exchange the Shared NG-U Termination Information over interfaces (NG, Xn, E1).
Capture how to support PDCP SN sync in the spec.