## Slide 1: TRS and URLLC summary open issues
<name>
<3GPP Role, Company name>

## Slide 2: Outline
Timing Resilience open issues
  RAN TSS reporting over NG: which procedures?
    RAN TSS reporting over F1: Same framework as NG?
  When Clock Quality Detail Level IE has value “clock quality metrics”, is any additional information included?
  Clock Quality Acceptance Criteria: how to encode
  RAN TSS Attributes: encoding of Clock Frequency Stability IE
  RAN TSS Attributes: encoding of Clock Accuracy IE
  Other miscellaneous proposals

## Slide 3: Timing Resiliency
RAN TSS reporting over NG: which procedures?
  AMF controlled
    Sol1: New AMF-initiated class 1 procedure + new gNB-initiated class 2 procedure (3 companies)
    Sol1A: Reuse AMF Configuration Update + RAN Configuration Update (1 company)
  No AMF control
    Sol2: Reuse NG Setup and RAN Configuration Update (2 companies)
    Sol2A: New gNB-initiated class 2 procedure (1 company)
RAN3 decision: TBD
RAN TSS reporting over F1: Same framework as NG?

## Slide 4: Timing Resiliency
When Clock Quality Detail Level IE has value “clock quality metrics”, is any additional information included?
  Option 1 (yes): Clock Quality Reporting Control Information IE indicates the specific clock quality metrics to deliver to the UE ; or
  Option 2 (no): All clock quality metrics supported by the gNB should be delivered to the UE
  Option 3 (unsure): Send LS to SA2
RAN3 decision: TBD

## Slide 5: Timing Resiliency
Clock Quality Acceptance Criteria: how to encode
  Option 1: Reuse the same encoding as the RAN Timing Synchronisation Status IE (i.e. the acceptance criteria is a set of thresholds)
  Option 2: OCTET STRING, details up to other WGs
RAN3 decision: TBD

## Slide 6: Timing Resiliency
RAN TSS Attributes: encoding of Clock Frequency Stability IE
  Option 1: INTEGER (0..65534, …) as defined in Table 4 of IEEE Std 1588
  Option 2: BIT STRING (SIZE (16)) as defined in Table 4 of IEEE Std 1588
RAN3 decision: TBD

## Slide 7: Timing Resiliency
RAN TSS Attributes: encoding of Clock Accuracy IE
  CHOICE allowing one or more of the following
    INTEGER with precise granularity, as low as e.g. 10ns or 25ns
    INTEGER with larger granularity, e.g. 100ns or 1us or 1ms
    ENUMERATED (or INTEGER) with values from Table 5 of IEEE Std 1588
    ENUMERATED with coarse values
    ENUMERATED with index values
  Maximum range: 1 second?
RAN3 decision: TBD
  Send LS to RAN2/SA2 if we converge on encoding of all RAN TSS attributes?

## Slide 8: Timing Resiliency
Other miscellaneous proposals
  Qualcomm P10: RAN3 to discuss if node level clock quality information includes clock quality information at gNB-CU-UP as well.
  ZTE P1: Introduce Time distribution Coverage area IE in the existing Time Synchronisation Assistance Information IE.
  Ericsson P3: The continuous reporting of the 5G Clock quality information to the UE during mobility. The clock quality related information is sent to the target RAN during handover procedure, and the target RAN feedbacks its clock quality information.
RAN3 decisions: TBD

## Slide 9: Outline
RAN Feedback open issues
  F1AP impacts
  Is proactive RAN feedback applicable/relevant after the initial establishment of the TSC QoS flow?
  Encoding of Burst Arrival Time Window IE
  Encoding of Burst Arrival Time Offset IE
  Encoding of Adjusted Periodicity IE
  Encoding of Periodicity Range IE
  Reactive feedback for UL
  Other miscellaneous proposals

## Slide 10: RAN Feedback
F1AP impacts
  For proactive case, which node determines the RAN feedback?
    Option 1: gNB-CU Nokia
    Option 2: gNB-DU (therefore F1AP impacts) Huawei
  For reactive case, which node determines the RAN feedback?
    Option 1: gNB-CU
    Option 2: gNB-DU (therefore F1AP impacts) Huawei
RAN3 decisions: TBD

## Slide 11: RAN Feedback
Handover
  Is proactive RAN feedback applicable/relevant after the initial establishment of the TSC QoS flow?
    Option 1: NO (Nokia, Ericsson)
      In NGAP, clarify (e.g. in semantics description) that target gNB shall ignore BAT Window and Periodicity Range IEs if received in a HANDOVER REQUEST message
      In XnAP, the BAT Window and Periodicity Range IEs are not needed in the TSC Assistance Information IE.
    Option 2: YES (Huawei, ZTE)
      For NGAP, include the TSC Traffic Characteristics Feedback (including the Burst Arrival Time Offset and the adjusted Periodicity) during handover procedure in the HANDOVER REQUEST ACKNOWLEDGE and PATH SWITCH REQUEST messages.
RAN3 decision: TBD

## Slide 12: RAN Feedback
Encoding of Burst Arrival Time Window IE
  Option 1: Window in reference to Burst Arrival Time IE
  Option 2: Timestamps
RAN3 decision: TBD
IE/Group Name | Presence | Range | IE type and reference | Semantics description
Earliest Burst Arrival Time | M |  | Burst Arrival Time 9.3.1.133 | Indicates the acceptable earliest arrival time of the first packet of the data burst at either the ingress of the RAN (downlink flow direction) or the egress of the UE (uplink flow direction).
Latest Burst Arrival Time | M |  | Burst Arrival Time 9.3.1.133 | Indicates the acceptable latest arrival time of the first packet of the data burst at either the ingress of the RAN (downlink flow direction) or the egress of the UE (uplink flow direction).
IE/Group Name | Presence | Range | IE type and reference | Semantics description
Burst Arrival Time Window Start | M |  | INTEGER (0..640000, …) | Start of the burst arrival time window calculated with reference to the Burst Arrival Time IE, expressed in units of 1 us. Integer values are negative.
Burst Arrival Time Window End | M |  | INTEGER (0..640000, …) | End of the burst arrival time window calculated with reference to the Burst Arrival Time IE, expressed in units of 1 us. Integer values are positive.

## Slide 13: RAN Feedback
Encoding of Burst Arrival Time Offset IE
  Option 1: Range from -640ms to +640ms in units of 1us
  Option 2: Range from -320ms to +320ms in units of 1us
Encoding of Adjusted Periodicity IE
  Same as Periodicity IE
RAN3 decision: TBD
IE/Group Name | Presence | Range | IE type and reference | Semantics description
Burst Arrival Time Offset | M |  | INTEGER(-320000..320000,…) | Burst Arrival Time Offset as specified in TS 23.501 [21], expressed in unit of 1us.
Adjusted Periodicity | O |  | Periodicity 9.3.1.132 | Not applicable to reactive RAN feedback.

## Slide 14: RAN Feedback
Encoding of Periodicity Range IE
  CHOICE between range and list
RAN3 decision: TBD
IE/Group Name | Presence | Range | IE type and reference | Semantics description
CHOICE Periodicity Range | M |  |  | 
>Bound Information |  |  |  | 
>>Periodicity Lower bound | M |  | Periodicity 9.3.1.132 | Indicates the acceptable lower bound of the periodicity range.
>>Periodicity Upper bound | M |  | Periodicity 9.3.1.132 | Indicates the acceptable upper bound of the periodicity range.
>Periodicity List |  |  |  | 
>>Allowed Periodicity List |  | 1..<maxnoofPeriodicities> |  | 
>>>Allowed Periodicity | M |  | Periodicity 9.3.1.132 | 

## Slide 15: RAN Feedback
Reactive feedback for UL
  Huawei P10: Editor’s note can be removed from the BL CR since RAN2 has agreed to either:
    re-use existing mechanism; or
    rely on gNB to determine the information (i.e. aim to not introduce new UE specific BAT reporting)
  Editor’s Note: Whether uplink is supported for reactive feedback is FFS pending RAN2.
RAN3 decision: TBD

## Slide 16: RAN Feedback
Other miscellaneous proposals
  E/// P5: RAN3 to discuss how NG-RAN should feedback the offsets to the burst arrive time and periodicity. In our view the DL feedback during QoS setup can be considered. The UL feedback and the very dynamic feedback are not feasible or useful.
  CATT P1: RAN3 discuss the maximum value of Periodicity and Periodicity Range
RAN3 decision: TBD

## Slide 17: Summary
TBD